## Slide 1: USING RAIN RADAR TO ESTIMATE THE SIZE OF FLOOD EVENTS
Luke Sutherland-Stacey Weather Radar NZ luke@weatherradar.co.nz
Tom Joseph Mott MacDonald
Geoff Austin University of Auckland g.Austin@Auckland.ac.nz
Ken Williams and Nick Brown, Auckland Healthy Waters

## Slide 2
Estimating Flood events with Rain Gauges
Resulting ARI estimates are spatially smooth
Is there more variability between the rain gauge locations which might better explain observed flooding?

## Slide 3
Two Radar systems are available in Auckland.
NZ Metservice: large permanent radar station
UoA: small (including mobile) research radars
Significant post processing is required to yield good quality radar data
MILSOM, G. et al. Project Storm 2 - A "world class" strategic planning tool. Water New Zealand Conference. 19-21 September, Energy Events Centre, Rotorua 2007.
Rainfall Quantification: Observation Systems
Metservice Radar
100km Range
University of Auckland Field Site (20 km range)

## Slide 4
Data handling
  Binary manufacturer radar data format
  Polar to GIS coordinate system (NZTM) mapping
Automatic QC
  Ground clutter (hills, buildings and trees)
  2nd trip echoes
  Other R/F transmitters
Advection between scans
Radar/Rain gauge correction
Radar Data preparation
Frame n
Frame n+1
Frame n+a (0<a<1)

## Slide 5
Post Event Reporting July 2015
Now Auckland Stormwater is investigating the use of Radar for stormwater event analysis.
An event July 2015 is the first to be investigated with this method.

## Slide 6
Current Work:
Post Event Reporting July 2015
Radar
Rain Gauge
… and big differences between using rain gauges and radar for calculation of ARI statistics.

## Slide 7
Current Work:
Post Event Reporting July 2015
Non- habitable RFS
Habitable RFS
… which can help to explain the location of Requests of Service.

## Slide 8
Current Work:
Post Event Reporting July 2015
Non- habitable RFS
Habitable RFS
… which can help to explain the location of Requests of Service.

## Slide 9
Current Work:
Post Event Reporting July 2015
Radar
… and highlights differences between using rain gauges and radar for calculation of ARI statistics…

## Slide 10
Where to from here?
Operational use of radar data planned. (H2KnowHow interface)
1 hours Radar Nowcasts for operational stormwater management

## Slide 11
Where to from here?
Operational use of radar data planned. (H2nOw-How interface)
1 hours Radar Nowcasts for operational stormwater management