## Slide 1: Scalable Cost-Effective Solutions To Restore Stream Ecosystems
Selwyn Streams:
Snake Creek
Powells Road
Mike Cope
WSP Opus
NZW SW Conference - 1 May 2019
Contributions from:
Emily Arthur-Moore – Fish & Game (W&WHT)
Robin Smith – Living Streams (DOC)
Greg Burrell – Instream Consulting
Alan Strong – Fish & Game

## Slide 2: Why Stream Restoration?
Natural corridors, less steep banks, planting, shading)
Habitat diversity
Instream features (e.g. pool-riffle)
Stream health (e.g. WQ, sediments)
Plus farm management, fencing,
vegetated strips / buffer zones

## Slide 3: The Trial Sites Selected (2017)
Trial waterway enhancement projects, to:
Improve habitat and water quality for freshwater biodiversity and mahinga kai; while
Maintaining the waterways
drainage function
Snake Creek
Powells Road
Consider the full range of values that our waterways can offer
Healthy waterways where New Zealanders can swim, fish and gather Kai
This is part of the national identity …

## Slide 4: The Trial Sites Selected (2017)
Two heavily modified lowland Canterbury waterways, both flowing to Te Waihora / Lake Ellesmere
Snake Creek, Silverstream catchment
Powells Road Drain, part of Arairira/LII catchment

## Slide 5: Regional Context
Te Waihora / Lake Ellesmere is/has
internationally important values
outstanding wildlife, with single most diverse bird habitat in the country
good stocks of native fisheries, including long and short-finned eels
High cultural significance
Canterbury regional plans for integrated management of land and water
Farm Environmental Plans - (“farming to limits”) - Good management Practice
Water Management Strategy, 2009 & Land and Water Regional Plan, 2015

## Slide 6: Why these Sites
Reasons for site selection for the trials include:
Spring-fed streams
Natural gravel bed
Sufficient slope to create diversity
Potential for fish and invertebrate species recovery
Broader drivers for Te Waihora / Lake Ellesmere and Selwyn River
Limited criticality in land drainage terms
Actively engaged landowner/farmer
Supportive District Council
A Kotuku

## Slide 7: Collaboration – an essential ingredient
To make the adjustments necessary for success
To go from ‘taking stuff out’ to ‘putting stuff in’
A change in mindset from all involved is needed
(landowners, council members, engineers, planners, operations staff, and the digger drivers …)
Plus understanding from the public
And thus
REQUIRES COLLABORATION
Leestons School

## Slide 8: The Problem
Erosion of over-
steepened banks
Sediment loads
silting up channels
REQUIRES INTEGRATED
SOLUTIONS
Macrophyte
issues
Weeds clogging
up channels and
catching sediment

## Slide 9: The Problem
Increased pollutants
Reduced flows and
heavy weed growth
REQUIRES CATCHMENT
SOLUTIONS
To create clean
gravels again
And restore amenity value, such as for swimming at Coes Ford

## Slide 10: Aim and Objectives
Overall Aim - To trial new ways of managing waterways, to improve habitat and water quality for freshwater biodiversity and mahinga kai, while maintaining the waterways drainage function.
Objectives
Improve habitat diversity
Enhancing fisheries, providing clean gravels for spawning
Improve water quality, raising environmental value
Enhancing broader amenity value for the catchment
Reduce sediment and contaminant loads
Providing shade to reduce macrophyte growth
Integrated land and water management across the wider catchment

## Slide 11: Waterway enhancement features
Some measures to help create living streams are:
Reshaping bank slopes
Instream features:
  Bank bags (filled with gravel or soil)
  Woody matter, e.g. for weirs or habitat
  Use of rock, e.g. to create islands and tumbling weirs
  Gravel features and creation of redds
  Planting for early shade (e.g. Carex Secta)
Planting of waterway banks for protection and shading
Farm management, fencing, buffer zones or wetlands (e.g. Owl Farm)

## Slide 12: Waterway enhancement features
Battering back of bank slopes
Re-battered slope assists with planting
Create low berm on one side, coir roll or similar to reduce soil runoff (seed banks)
Re-batter slope (one side is good) with excavator

## Slide 13: Waterway enhancement features
Narrowed sections for increased velocities
Bank bags
Stabilises bank slope toe, forms a base for planting
Easily placed by hand

## Slide 14: Waterway enhancement features
Creation of wooden V-weirs to focus flow to the channel centre
Wooden weirs or habitat features
Inclusion of root wads for aquatic habitat
EU Water Framework Directive requires conditions close to ‘natural’, with woody matter playing a role

## Slide 15: Waterway enhancement features
Boulder weirs and Rock islands

## Slide 16: Waterway enhancement features
Clean gravels in narrow sections, with varied structure, habitat and shading is encouraging spawning
Encouraging creation of redds
Trout are already creating redds in the narrow sections
The resistance to flow from the waterway features is minimal

## Slide 17: Waterway enhancement features
Lack of shade, nutrients and slow flowing water, leads to macrophyte growth
Sedge planting, such as Carex secta, is quick to establish and can provide shading within 1-2 seasons
The importance of shading

## Slide 18: Waterway enhancement features
In no time at
all - from this …
To this …
Planting Carex secta is clearly a happy-inducing past time!
Planting for early shading

## Slide 19: Waterway enhancement features
Planting of waterway banks
Grass seeding at early stage to reduce bank erosion and soil loss to the waterway
Planting of natives on the banks for shading, but maintaining access for maintenance and farm management
Use of fast growing natives

## Slide 20: Waterway enhancement features
Evolution of works at Powells Road

## Slide 21: Constraints on the works
Crack Willow has directed high flows onto left bank and caused scouring and sediment loss – resulting in undermining of the power poles
Crack Willow on right bank removed
Flows directed away from left bank
Toe of bank secured with hesian bags
Scour hole filled with gravel and cobbles
Topsoiled and seeded to stabilise bank

## Slide 22: Looking forward
Catchment-wide restoration
Expand to larger streams and rivers
GIS system to identify stream potential for restoration works
More urban settings?
Predicted surface flow paths
Clearing out Sediment Traps
Monitoring and sampling
High sediment loads
Carex secta – sustainable?
Modelling of surface runoff

## Slide 23: Looking forward - so what can I do?
So how to contribute more to enhancing our waterways, to better recognise the broad range of values that they can offer.
Question the status quo?
Gain improved knowledge of the locations and issues
Develop more integrated and sustainable approaches
Create objectives and actions that reflect the new approach
Key elements
Communicate, educate and understand
Collaborate for win-win outcomes
Sell the idea – it will need some initial funding
A collective paradigm shift in mindset