## Slide 1
Aisling (Ash) O’Sullivan, Ph.D.
Ecological Engineer, University of Canterbury
Urban Stormater Treatment
Industry

## Slide 2
HydroEco’s Urban Stormwater Research (since 2006)
Stormwater characterisation
Real-time in-stream monitoring
Experiments to generate data from different pavement & roof surfaces
Modelling (e.g. SWMM, MEDUSA) to predict contaminant behaviour as a function of rainfall characteristics and impermeable surface types
Treatment and hydraulic efficiencies of stormwater treatment systems
LCA modelling of treatment systems
Understand stormwater dynamics and effective treatment for mitigating contamination and improve ecosystem health

## Slide 3: Current UC Engineering Researchers
Academic staff:
Tom Cochrane
Aisling (Ash) O’Sullivan
Frances Charters
Ricardo Bello Mendoza
Student researchers:
Forrest Bilek
Fabio Silveira
Rachel Sykes
Sergio Hansen
Julian Maranan
Will Heffernan
Elise Howe
Melissa Klok
Jess Aldridge
Technical support staff:
Peter McGuigan
Aude Thierry
Previous research students:
Too many to list!
Main Stormwater Research Areas:
Monitoring (quantifying signatures)
Modelling (predict pollutant loads)
Treatment technologies (provide solutions)

## Slide 4
Water is vector (carrier) of materials – this includes pollutants societies generate
This includes urban runoff (Stormwater)
ALL “civil” engineers affect water quality
Notes: As the video highlighted, the quality of our waterways is concerning.
Yes, tater (as we know) is essential for all life – but is a very complex resource!
This figure shows the main pathways in which water moves in the environment so any activity we do, affects the quantity AND quality of our water resources

## Slide 5: 1. Monitoring (quantify signatures)
and metals
(Zn and Cu)
Notes: Started in-stream

## Slide 6: Continuous stream monitoring systems
Components:
Network of radio transmitters
Parameter-specific sensors
Water level meters
Computer base station for logging data
Data interfacing onto dedicated webpage
Complementary weather station and automatic sampler
sampler
Within streams (mixed concentrations)

## Slide 7
How much pollutants originate from different urban surfaces?
Where and what should we target?
What are the possible pollutant load reduction from implementing different management options?
Catchment
Property
Surfaces
Research questions
Notes: An event-based model that relates individual contaminants to climate characteristics, and can screen for benefits provided by source reduction as well as treatment

## Slide 8
Stormwater is the largest polluter of urban waterways globally – metals are toxic to waterways
www.ecan.govt.nz
Heavy Metal Sources
Atmospheric deposition (wind blown particles that settle)
Vehicle tyres (zinc) and brakes (copper)
Metallic roofs and guttering
Metal roof types (old & new)
Coloursteel™
Zincalume™
Galvanised steel (iron) – painted & unpainted
Copper
Notes: When it rains toxic metals dissolve from all metal roofs (as well as some contribution from roads from vehicle wear)
Different sources of heavy metals have different concentrations (or strengths/loads) of metals
MOST metals come from roofs (even though some from roads) so we decided to target roof stormwater runoff.
Zinc-based roofing material produced the highest zinc concentrations, typically about 3-5 times higher than road
Between 2-9 kg Zn/ha *per rain event* dissolve from metal roofs and discharge into nearby waterways.
Councils identified this as a key impediment to restoring waterways.

## Slide 9
25 rain events
9 rain events
9+ rain events
Roofs | Roads | Carparks
Galvanised (Zn) Copper Concrete/inert (old/new/painted) | Major arterial Minor arterial Collector Local | Commercial Industrial Std Industrial Manoeuvring
From individual surfaces (source concentrations)
Notes: Just a quick view of all the Chch sampling sites:
Across different land uses
Across different surface types
This is an internationally relevant dataset

## Slide 10: Monitoring data revealed
Material properties have a significant effect on runoff quality – opportunity for source reduction through material choice/maintenance
Particle size distribution varies significantly for the same surface type – important to characterise to understand risk to treatment performance
Metals partitioning varies by surface type – important to characterise so appropriate treatment is selected
Very high pollutant concentrations observed, orders of magnitude above receiving environment guideline values
Notes: 4. See that how it rains drives pollutant generation
5. Dilution and mixing in the environment not enough – need to actively reduce pollutant concentrations before they reach the receiving waterway

## Slide 11: 2. Modelling
Impermeable surfaces directly feeding runoff to urban waterways
Predict the hotspots and quantify where most contaminants originate from

## Slide 12: 2. MEDUSA pollutant load model
Modelled Estimates of Discharges for Urban Stormwater Assessments
What is the spatial distribution of where pollutants are being generated?
Predict change in pollutant loads under future conditions, e.g.:
1. Climate change
2. Different mgt. scenarios
Create a useful tool to delineate pollutant hotspots in the catchment
Research questions:

## Slide 13: Motivation for MEDUSA model tool
Response of pollutant concentrations to how it rains (duration, intensity etc.).
Challenges of previous models, which typically:
  Aggregate by land use activity
    But the dataset shows surface type is a key driver…
  Calculate annual load (not event)
    But we design our treatment system capacity on an event basis…
Need guidance on where and what stormwater management is needed
Notes: Response of pollutant concentrations to how it rains
Address some of the limitation of previous models, which typically:
  Aggregate by land use activity
    But the dataset shows surface type is a key driver…
  Calculate annual load (not event)
    But we design our treatment system capacity on an event basis…
Need guidance on where and what stormwater management is needed
Need to move from a catchment scale through to an individual surface scale to enable property owners and stormwater managers to make more effective decisions

## Slide 14: MEDUSA model framework
Event-based model
Individual surfaces (roofs, roads, carparks) contributing to SW system
Rainfall characteristics: intensity, duration, antecedent dry period, rainfall pH
Pollutants: Total suspended solids (TSS), total and dissolved zinc (Zn), and copper (Cu)
Coefficients to describe relationship between rainfall characteristic and generated contaminant load
  Use untreated runoff data to define these values
  Data from Okeover, Addington, Heathcote catchments (new data in Timaru)
Notes: Just to summarise:
MEDUSA predicts TSS, total and dissolved copper and zinc loads for each individual rain events. It calculates these loads from individual roof, road and carparks surfaces within a catchment.
Individual equations used to estimate each contaminant from the climate characteristics (instead of assumed ratio of metals to TSS)
Benefits of an event–based model:
>> This one still allows annual loads to be calculated
A note about what this Model is, and isn’t:
Modelled contaminant load at the discharge point as it is about to enter the waterway, so not In-stream water quality (in-stream transport and mixing not included), and in-stream contributions (e.g. bank erosion contributing TSS) not included here either
Calculates load contribution from individual delineated surfaces – not including small hardstand areas on private property or overland flow during larger events
Could extend the model to include other contaminants but would need to identify the contaminant relationships to rainfall characteristics etc. from literature.

## Slide 15: MEDUSA model framework
Rainfall characteristics
Model coefficients
Estimated Load
EQUATIONS:
Cu
Zn
TSS
Cu
Zn
TSS
Cu
Zn
TSS
+ + +
+ + +
Carpark surfaces
Road surfaces
Roof surfaces
Surface characteristics:
Material/usage
Area
Shape
Where its runoff enters waterway
Empirical coefficients for:
Pollutant build-up
Pollutant wash-off
Rainfall duration
Antecedent dry period
Rainfall intensity
Rainfall pH
Notes: The model that I have developed is called MEDUSA – Modelled Estimates of Discharges for Urban Stormwater Assessments
Using mathematical relationships to simulate the way contaminants build up and wash off from individual urban surfaces during rainfall.
The model focuses on TSS, copper and zinc, because of significant concern to environmental health and in-stream monitoring has shown these to be elevated compared to Water Quality guideline values.
Take roof surfaces
Calculate load for each surface with particular equations, Inputs are coefficients and rainfall characteristics
Summed loads for each discharge point, and sum these for whole catchment load
This forms baseline case for catchment (i.e. as current condition)

## Slide 16: Metal roofs at UC
Metal roof types (old & new)
Coloursteel
Zincalume™
Galvanised steel (iron) – painted & unpainted
Copper
Notes: Blue and green are the only NON metal roofs in the Okover catchment – that is the stream you likely walked over to get to this presentation is receiving all the stormwater from these metals roofs UNTREATED!
ALL of these metals roofs (both ‘old’ AND new leach metals directly from the roof into the nearby Okeover stream untreated – we know because we’ve measured them for years, along with other roofs in ChCh
We have also modelled how much metals leach from our roofs in Christchurch
“In Christchurch, roofs contribute 65% of stormwater zinc that damages rivers.
New, renewed and future consents now require stormwater to be treated before leaving the property.”

## Slide 17
MEDUSA application (Okeover, Addington, all Heathcote)
Notes: And just to show the equivalent output for Addington carparks and roofs – we started off applying the model to the 62 ha Okoever catchment, now this is for the 240 ha Addington, Heathcote covers half the city. The model is scalable.
This map has helped stormwater managers decide where to focus their efforts and also support a range of management approaches – where source reduction might be effective, where clustered, centralised treatment might be appropriate for an area of surfaces, or what size threshold policies could be set at to require on-site treatment of runoff, for example.

## Slide 18: 3. Treatment technologies
Reduction at Source
- Green roofs
- Permeable paving
- Repainting roofs
- Other?
On-site Management
- Filters
- Infiltration swale
- Raingarden
Off-site Management
- Wetlands
- Dry basins
- Wet ponds
Notes: Options for reducing these contaminant loads
Load = conc x flow so reduce one or the other to reduce load
Spectrum from source reduction to off-site treatment
Can be used in combination

## Slide 19: Current Treatment studies
Wigram Retention Basin (WRB):
Pre- and post upgrade (3 new wetland cells) performance monitoring
Complementary flume experiment: changes in water quality under different groundwater conditions lined with sediment taken from Haytons Stream and WRB
Storminator: in-line downpipe treatment system – 1st Place 2019 Stormwater Innovation Award
Quantifying treatment performance in various sized units around Christchurch since 2017
Proprietary treatment systems: Stormfilter, Storminator, Jellyfish and Filterra:
Performance monitoring to characterise the variability (influent load variability (surface, climate), treatment system variability, operations and maintenance variability)
Geochemical modelling of treatment mechanisms of the Storminator
Identify the key treatment mechanisms and cartridge re-generation potential
Life Cycle Assessment Modelling (Environmental Impact) of the Storminator and Stormfilter
Quantify the 18 different environmental LCA metrics for different proprietary treatment systems
Why focus on metals?

## Slide 20
Galvanised roofs are the largest contributor of ecotoxic Zn to urban waterways
www.ecan.govt.nz
Roofs contribute 65% of all Zn in the urban environment
Toxic
Level (15 ug Zn/L)
Zinc
Copper
Notes: When it rains toxic metals dissolve from all metal roofs (as well as some contribution from roads from vehicle wear)
Different sources of heavy metals have different concentrations (or strengths/loads) of metals
MOST metals come from roofs (even though some from roads) so we decided to target roof stormwater runoff.
Zinc-based roofing material produced the highest zinc concentrations, typically about 3-5 times higher than road
Between 2-9 kg Zn/ha *per rain event* dissolve from metal roofs and discharge into nearby waterways.
Councils identified this as a key impediment to restoring waterways.

## Slide 21
The Piano
Knox Church
Engineering E8 & E9- UC
High Voltage Lab - UC
Sumner residence
Notes: Might recognise some of these copper and zinc roofs nearby?
“In Christchurch, roofs contribute 65% of stormwater zinc that damages rivers.
New, renewed and future consents now require stormwater to be treated before leaving the property.”

## Slide 22: The extent of the Problem
Most roofs in NZ are metal; com/industr (95%) & residential (80%)
Roof stormwater = dissolved metals
Toxic to the aquatic environment = urban rivers
Consumes natural capital
New regulation to meet National Policy Statement Freshwater Levels (LWRP and TA By-Laws)
Property owners need consent to discharge the stormwater.
Regulators require adequate stormwater treatment before granting consents – new & renewed.
The Roofing industry is under consumer pressure to mitigate its material impacts.
Notes: These metals are in dissolved form and are going untreated into our urban waterways
Dissolved metals are also difficult to treat and our current stormwater treatment systems where they exist don’t deal with them very well-they simply pass through them
This means regulators are increasingly tightening up on building owners to manage these dissolved metals before they enter the Council stormwater system.

## Slide 23: On-site treatment devices
Challenges:
  Expensive
  Large footprint
  Don’t remove much dissolved metals
  Use new materials
  Disrupt business
  Requires pipes and power
Notes: Costs to replace metal roofs are prohibitive and cause significant business disruption.
Painting roofs is also costly.
Stormwater treatment systems are expensive, command valuable space, incur high maintenance and rarely treat the dissolved most ecotoxic
metal forms. e.g. raingardens….newest ones in ChCh – The Commons and UC

## Slide 24: The Storminator™ –
  Downpipe treatment system - instantaneous treatment
  Uses food waste products as a reactive media cartridge
  Highly efficient (>80% removal of dissolved metals)
  Quick to install & retrofittable - no business disruption
Storminator unit
Clean water to waterway
Roof stormwater
Our Solution -
Notes: Leveraged on previous research using waste shells to treat v nasty mine drainage and then in some raingardens as the treatment media.
The ‘Storminator™ is a retrofit inline treatment solution that removes the majority of toxic dissolved metals from roof runoff so overcomes the challenges of existing stormwater treatment systems.
The design uses ‘off-the shelfʼ PVC piping & waste media (shells).
Systems are easily scaled to any metal roof size and condition.
For property owners it is cheap, highly effective and can be retrofitted to existing buildings. It commands no horizontal footprint.
So more insects, koura and fish can survive and thrive in the nearby waterway.”
>94,000 tonnes/yr of greenshell mussel waste. 50% disposed to landfill @$100/tonne
Some shells sold as fertiliser and landscaping gravel. Blue shells recently used in compost mix for vineyards (10 tonnes/day). Only 50% re-used – rest to landfill, costly.

## Slide 25: Unique Features of Our Solution
Product Features:
Removes >> 80% dissolved metals
Retrofittable, small footprint
Uses food waste, i.e. shells
Business Features:
Low cost; < ¼ other solutions
Replacement cartridges available
Certification can reduce monitoring requirements for consent compliance
100% waste shells media
50% waste shells media
Notes: Coffee grinds (other C wastes) may also enhance Cu removal
Effluent conc 150 ug/L TZn..

## Slide 26: The Storminator™ - 7 Systems Installed & Operated
Hagley College Roofs:
Colorsteel & Zincalume
2 units: 150 mm ø X 1.5 m cartridge
UC Roofs:
Zincalume & Copper
4 units: 100 mm ø X 1.0 m cartridge
Tower junction (Ngāi Tahu) Roof: Zincalume
1 unit: 225 mm ø X 1.5 m cartridge
(“Super-Storminator™”)
Notes: Early Adopters
ECan have financially supported R&D of the Storminator™ since 2018 and we currently are validating multiple systems for them.
The largest galvanizing company in NZ has also commissioned > 4 systems™ for later this year.
Other councils have requested units (Tauranga, Timaru)

## Slide 27: Current Development
Regional Councils
City/District Councils
Ministry for the Environment & Ministry for Awesome
Business owners


We’re already supported by….
Units | #
Operational | 7+
Further orders confirmed | 4
Additional orders: 2 more councils (Tauranga, Timaru) | 
R&D Funding | 
ECan | 
KiwiNet (& UC) | 
Callaghan Innovation | 


PCT patent filed & trademarked
AJ Park (patenting)

Endorsements
Water NZ Stormwater Group via Innovation of the Year (2019)
ChCh West Melton Zone Committee (Canterbury Water Management Strategy)
1st
Notes: Letters of Support
MfE
ECan
CCC
Ngai Tahu
They oversee and champion the implementation of recommendations by Environment Canterbury and other Canterbury Water Management Strategy partners
Water zone committees develop actions and tactics to deliver on the 10 targets of the Canterbury Water Management Strategy in their zone.
Water zone committees recommend actions and tactics to councils and other organisations involved in water management, which are recorded in Zone Implementation Programmes (ZIPs).

## Slide 28: The Storminator™ “a simple solution to a difficult problem”
Winners of the 2019 National Stormwater Innovation Award
Notes: Partner w/ SW360

## Slide 29: Future stormwater research?
Working on simple and sustainable solutions for nutrient treatment
Applying MEDUSA beyond ChCh
Source control stormwater runoff in other (non-urban) catchments
Further LCA modelling
Storminator to international certification
My Wish list:
  Constructed Wetland System at UC
  Floating wetlands with mussel shells
  Metal roofs phased out
  Stormwater reuse (as non-potable supply)
Questions and feedback most welcome

## Slide 31: How does our zinc level compare to elsewhere?
Notes: This also helps confirm that trial and studies done elsewhere are likely to be appropriate and applicable

## Slide 32
Roof Type | Catchment | Cond. | Total zinc (ug/L) | Dissolved zinc (ug/L)
Concrete | Heathcote | FF | 380 (290-480) | 323 (230-480)
 |  | SS | 315 (174-470) | 284 (161-400)
Concrete | Okeover | FF | 21 (9.2-44) | 17 (5.6-44)
 |  | SS | 15 (5.4-36) | 9.6 (2.8-25)
Coloursteel® old | Heathcote | FF | 2,415 (810-4,500) | 2,330 (810-4,500)
 |  | SS | 644 (330-880) | 640 (330-860)
Coloursteel® new | Heathcote | FF | 503 (186-1,070) | 469 (186-1,010)
 |  | SS | 154 (47-290) | 111 (44-250)
Galvanised painted | Heathcote | FF | 1,879 (980-4,800) | 1,827 (980-4,800)
 |  | SS | 342 (153-480) | 337 (153-480)
Galvanised painted | Okeover | FF | 1,005 (372-2,369) | 993 (372-2,369)
 |  | SS | 335 (75-1,057) | 332 (75-1,057)
Galvanised unpainted new | Addington | FF | 4,782 (410-12,600) | 4,442 (410-11,400)
 |  | SS | 1,085 (950-1,310) | 1,018 (940-1,120)
Galvanised unpainted old | Addington | FF | 32,338 (11,700-56,000) | 28,250 (10,700-53,000)
 |  | SS | 5,920 (2,400-8,700) | 5,900 (2,300-8,700)
Copper | Okeover | FF | 83 (36-292) | 65 (16-207)
 |  | SS | 23 (5-147) | 16 (4.2-44)
Notes: 1. Coloursteel new vs Coloursteel old – difference seen
2. Coloursteel new vs concrete – even coated zinc-based material produces higher zinc than inert material (so not just atmospheric dep contribution)
3. Galv painted roof sampled in two different catchments produced similar results – reinforcing applicability of calibrated model beyond one catchment
4. Galv unpainted even if brand new still produces more zinc than older coated roof
5. A poor condition unpainted galv roof can produce incredibly high amounts of zinc, mostly in dissolved form
6. We realised the concrete roof we sampled in Heathcote had galv fittings for the spouting, and this raised the zinc concentrations significantly above an inert roof with inert (e.g. PVC) spouting

## Slide 33
Stormwater reused
Stormwater reuse allocation from 17 stormwater recycling systems across Australia accounts for 15% (Sydney) - 45% (Gold Coast) of water use. Catchment sizes (5-500 ha) not influential.

## Slide 34
Stormwater recycling schemes
Type | Examples
Dual reticulation (using 3rd pipe network) following treatment | 40 schemes to supply 12% of Sydney’s water e.g. 56,000 dwellings in Rouse Hill, NSW
Potable distribution network (Centralised harvesting & treatment) | 13 km2 catchment yielded 8.5-14.2 ML/day from runoff 239-400 mm/yr (25% annual rainfall harvested)
Advanced wastewater treatment via membrane filtration | Brisbane’s 3 water supply reservoirs
ASR (50% DOC removal) | Mixed residential & industrial catchment yielded 0.8 x 106m3/day from runoff 450 mm/yr Substituting 1.2 GL/yr of Adelaide’s stressed groundwater reserves with recycled stormwater
Abstracting 411 L p.e. daily – 161 L industry = 250 L/d individual use
Runoff 1807 L p.e. daily >factor of 4 daily demand; surplus

## Slide 35
Stormwater network
Roof guttering
Downpipe
Discharge outlet
Leaf guard (deflects debris)
Connector join
Housing for inlet sampling
Inlet sampling bottle, tube and mini funnel
Perforated end cap
Drainage funnel
Self-supporting sleeve with cut for bottle emplacement
Ground surface
Effluent sampling bottle
Roof runoff from gutter (pollutant load dependent on roof material, rainfall characteristics and contributing area)
Media cartridge (diameter, length and media type optimized to roof runoff)
By-pass port (for excess inflow during high intensity rain events)
By-pass tube (for excess inflow during high intensity rain events)

## Slide 36
Approach
 Retroffitable & Adaptive – applied to any old or new roof
 Treats the ‘tough stuff’ > 75 % dissolved metals
 Fast Hydraulic throughput (> 39 m/hr particle size ≥2.36 mm)
 Customisable – units sized to roof size
 By-pass – GPT and overflow/by-pass
 Cheap – ~ 1/3rd cost of proprietary devices
 Simple solution to a ubiquitous problem using ‘off-the shelf’ PVC piping & connector components’
 Accessible – via UC currently (see me after for Conference Promo!)
Uniqueness
 Light weight and self-supporting (< 30 kg)
 Innovative – only downpipe treatment system known
 Quick to install and no disruption to business
 No ‘footprint’ – in-line with existing downpipe
 Sustainable – media cartridge (replaceable) uses waste shells
 Field-validated on various ChCh metal (Zn, Cu) roof types & sizes
 PCT patent app. trademarked™ & Co. est.
Application
 Council & MfE supported
 Industry Orders (galvanizing plants) and International enquiries
 Guided to Certification by leading NZ Stormwater provider
Value
 Low maintenance (~ 2 yr cartridge), ‘recycles’ other industries waste
The Storminator™ - simplest, sustainable way to ‘battle’ waterways pollution from roofs
Product Summary