## Slide 1: How will climate change affect our two waters?
James Hughes

## Slide 2: Agenda
Some background
About the project
Impacts summary
Key implications
Regional analysis
Some recommendations (what may all this mean, and how should we respond?)
Notes: Internationally: Hurricane Harvey, Irma and
Locally we had Debbie and cook
2 NZ examples: 1 of direct risk, another of residual risk

## Slide 3: Climate change

## Slide 4: Data

## Slide 5
Source: Fuss et al, 2014

## Slide 6: So what does this mean?
World Economic Forum: Global Risks Report 2018

## Slide 8: Is unprecedented the new normal?
The past is not a good indicator of the future
Direct / indirect / residual risks
ICNZ: $234M in insured losses 2017;
ICNZ: $72M in May event, $225M to Oct 2018
What about uninsured?
Notes: Internationally: Hurricane Harvey, Irma and
Locally we had Debbie and cook
2 NZ examples: 1 of direct risk, another of residual risk
2017 auck and taurang 4th wettest year since records began
54 NZ weather stations have just recorded the warmest summer on record

## Slide 9
364 river control, flood protection, and land drainage schemes
protect some 1.5 million hectares of land
collective replacement value of $2.3 billion
Notes: Levin, edgecumbe, whakatane, buller, whanganui, palmerston north
STOPBANKS! Lets start with this
Stopbanks are not assessed as part of building code
They are not required to undergo a dam break assessment (or PIC – probable impact category)
Are controlled by Regional Council engineers….but no national guidance
What would have happened if this occurred at night time?
HOW ARE WE MANAGING THE RESIDUAL RISK of all the townships that exist behind floodbanks.

## Slide 10: Edgecumbe flood 2017
… the Panel has concluded that the historic framework which has governed the development of the Rangitāiki River Control Scheme is at or near the end of its useful life. Frameworks now being more widely adopted look towards allowing greater room for rivers to move. This change is underlined by the near-certainty that climate change is leading to more severe and more frequent extreme weather events of the sort that occurred in April this year.
Rangitaiki River Scheme Review, 2017

## Slide 11
Start with haumoana and come back to it later?
Complexity ?

## Slide 12: Complex systems
Ecosystem?
Food sources?
Aesthetic value?
Water supply?
Properties and assets ?
Contact recreation?

## Slide 13: The research project

## Slide 14: Project overview - background
This project: Stormwater, wastewater, climate change: Impacts on our economy, environment, culture and society
NSC - Deep South Challenge
Impacts & implications stem of research
Emerged from the NSC Climate Change and Stormwater and Wastewater Systems report
Project team: James Hughes (T+T)
Rob Bell and Paula Blackett: (NIWA)
  Adolf Stroombergen: (Infometrics Consulting)
  Katherine Heays and Erica Olesson: (T+T)

## Slide 15: Project overview - methodology

## Slide 16: Working group
Paula Blackett (NIWA); Mark Bishop (Watercare); Blair Dickie (Waikato Regional Council); Iain White (Waikato University); Tumanako Faaui (Ngāti Whakahemo); Rob Bell (NIWA); Adolf Stroombergen (Infometrics); Sue Ellen Fenelon (MfE); Gavin Palmer (Otago Regional Council); Tom Cochrane (Canterbury University); Stu Farrant (Morphum); Liam Foster (Opus); Troy Brockbank (Stormwater 360 / Opus).

## Slide 17: Framing risk, impacts, implications
Notes: Give example: Summary: Sea level rise, can lead to rising groundwater (hazard) that can impact underground pipes (exposure), and depending on pipe material (vulnerability), this can lead to an impact (eg corrosion, infiltration), as well as a range of implications (increased costs, reduced LOS, WQ implications etc)

## Slide 18: Relevant climate drivers
Climate change hazards / stressor | Relevance to SW/WW systems | Simplified inclusion ‘theme’ in study
Increased frequency and intensity of rainfall events | High | Increased rainfall
Increased volume of rainfall events | High | 
Drought followed by high intensity rain | High | 
Increased frequency and intensity of droughts | High | Decreased rainfall
Increased numbers of dry days | High | 
Sea-level rise and coastal flooding (waves, storm-tide) | High | Sea level rise
Sea-level rise/high-tide inundation & rising groundwater | High | 
Temperature increase | High | Increased temperature
Changing seasons (Earlier springs, longer frost free summers) | Medium | 
Increase in severe winds | Medium | Increased wind (Included where relevant)
Accelerating coastal erosion | Medium | 
Shorter duration of seasonal snow line | Low | 
Reduction in glacier length and ice volume | Low | 
Ocean currents change | Low | 
Ocean temperatures increase | Low | 

## Slide 19: SW and WW assets considered
 | Included in study
Conveyance | Overland flow paths (including roadside channels) Piped networks (including catchpits/sumps, manholes, inlets and outlets, pump stations) Constructed channels Stopbanks
Treatment | Stormwater quality improvement devices (such as constructed wetlands, ponds, rain gardens, swales) Proprietary filter devices
Other | Construction stormwater management systems Infiltration devices
 | Included in study
Conveyance | Separated gravity system Combined gravity system Pressure system Pump stations
Treatment | Treatment plants and processes – including primary, secondary tertiary, oxidation ponds, sludge management etc On site wastewater systems
Stormwater
Wastewater

## Slide 20: Impacts on stormwater systems

## Slide 21: Key stormwater conveyance impacts
Increased flooding
Damage to infrastructure
Scour and erosion
Increased contaminant concentrations
Resuspension of sediments
Raised groundwater table
Reduced baseflows
Warmer water temperatures

## Slide 22: Increased intense rainfall and flooding
Increased frequency of intense rainfall events - leading to:
Increased flows and surface flooding
Increased frequency of groundwater level changes
Increased soil erosion and landslides
Exceedance of capacity of waterways leading to changing flood plains, damage to property and infrastructure
Changes in mean rainfall affects the initial water retention capacity of pervious surfaces, shifting the runoff response of a catchment

## Slide 23: Infrastructure damage
Extreme rain can come with extreme wind, leading to compounding impacts
Windfall, debris, blockages, power outages.
Landslides can also damage infrastructure

## Slide 24: Scour and erosion
Increases to volume, duration and velocity of flows cause stream erosion and degraded habitats
Heightened erosion risk with increased rainfall or altered wetting and drying patterns
Erosion and scour has dual negative impacts, where the act of erosion can cause significant damage to the infrastructure or loss of land as well as generating pollution

## Slide 25: Contaminant loading
Scour and erosion causes TSS increase and can also initiate the resuspension of historical sediment
Higher velocities collect more rubbish and debris from around the catchment, causing blockages
Pollutants of many types: Nutrients, bacteria and viruses, oil and grease, total dissolved metals, organics, pesticides and gross pollutant loadings may enter waterways more frequently as the catchment hydrology changes
Higher flows, mean increased flushing

## Slide 26: Reduced rainfall impacts
Higher peak flows: Reduced rainfall and higher temperatures influence evaporation rates from organic surfaces and hence the initial water retention capacity and shifting the runoff response time of a catchment, where dry land results in faster and higher peak flows
Behaviour changes: Reduction in rainfall frequency can result in changing attitudes towards waterways and overland flow paths. Property owners may be more likely to encroach on floodplains if they are active less frequently.
Stream health will be impacted as watercourses receive more variation in flowrates, and experience sedimentation and weed growth as well as changes in type/distribution of pest species

## Slide 27: Sea Level Rise impacts
Increased flooding: Waterway and infrastructure capacity will be impacted, where submerged infrastructure near coastal edge.
Raised groundwater table: may cause increased groundwater infiltration into the stormwater system, impact on infrastructure (flotation), soakage capacity, and increase liquefaction risk.
Damage to infrastructure: Coastal erosion is likely to be accelerated where it is already occurring and erosion may become a problem over time in coastal areas that are presently either stable or are advancing

## Slide 28: Temperature impacts
Reduced baseflow: Warmer temperatures may result in decreased runoff volumes, as evaporation and evapotranspiration reduce – leading to lower baseflow
Warmer runoff water temperatures: Rising atmospheric temperatures will increase runoff temperatures – and lead to increased nutrient impacts and eutrophication.

## Slide 29: Key SW treatment impacts
Higher peak flows
Increased contaminant loadings
Reduced capacities
Salinity impacts
Rising groundwater
Increased evapotranspiration
Plant stress
Eutrohpication

## Slide 30: Increased rainfall
Higher peak flows: Reduced LOS in general
Devices designed for volume control, such as ponds and wetlands may be unable to accommodate increased runoff volumes if they do not have the opportunity to drain fully before the next large rainfall event occurs.
Device flooding, scour, and damage to aquatic plants and habitat.

## Slide 31: Dry followed by wet
Increased storm intensity with prolonged dry periods between events: will likely result increased concentrations in first flush flows
Reduced efficiency of devices
Shorter residence times
Note: Offline wetlands and raingardens that have been designed to current best practice can be well suited to respond to short duration high intensity events as the majority of contaminants are delivered in the first stage of rainfall runoff before bypass engaged.

## Slide 32: Raingardens
Raingardens operate best when capturing frequent smaller events. Less frequent events with higher peak flows may result in reduced level of service for raingardens
Raingardens will receive more variation in water volumes, increased water temperatures and increased evaporation as a result of reduced rainfall and higher temperatures.
Effectiveness of plant species may vary as rainfall and temperatures change.

## Slide 33: Impacts on wetlands
Increased degree of eutrophication and greater frequency of algal blooms
Altering of lake margin habitats, including wetlands, with either increased or decreased rainfall
Negative impacts on aquatic macrophytes, particularly native species, if lake levels fall
Changing plant species as water level fluctuations change
Increased ranges of pest species (eg, carp), placing even more pressure on aquatic ecosystems

## Slide 34: Case Study - Whangamarino
Whangamarino Wetland (left, source: DOC) and nearby fish mortality during 2017 floods (right, source: Andrew Rumsby, PDP & Waikato Regional Council)

## Slide 35: Impacts on wastewater systems

## Slide 36: WW Conveyance
Increased incidences of overflows
Blockages within systems due to low flows
Corrosion risk
Flotation of pipes
GW ingress
Infrastructure damage

## Slide 37: Reduced rainfall and increased temp
Longer dry spells will increase the likelihood of blockages and related dry weather overflows.
Experienced and studied extensively in places such as Australia, South Africa and California that have experienced prolonged drought
Prolonged drought can result in water restrictions being put in place and the adoption of sustainable practices such as greywater reuse, low flush toilets.
This implementation of source management practices decreases wastewater flow.
This reduction in flow is compounded by the reduction in I&I flows that enter the network from stormwater sources.

## Slide 38: LA Case Study (2015)
Notes: Water conservation measures instigated in 2015
Caused widespread corrosion and odours while water suppliers have suffered revenue shortfalls.
Inadequate flushing flows caused build-up of solids resulting in pipe corrosion, and higher concentration flow caused faster wear in pumping stations.
Heightened risk of blockage and corrosion prevention works have increased maintenance work
Water starved trees have been found to penetrate sewer systems more frequently in search of water
Wastewater treatment plants reportedly struggled with poor influent wastewater quality, due to elevated concentrations of total dissolved solids, nitrogen species and carbon

## Slide 39: WW treatment plant impacts
Increased inflows
Storm related outages
Increased strength of influent, affecting treatment efficiencies and discharges
Changes to biological processes
Odours
Reduction of assimilative capacity of receiving environments

## Slide 40: Implications

## Slide 41: Implications

## Slide 42: Types of implications
Insurance levies rising, or assets become uninsurable
Increased stranded assets
Under utilisation of assets
Retreat or relocation
Financial cost of damage from flooding – residential and business
Community, cultural and psycho-social cost of impacts
Environmental impact (from damaged infrastructure, increased spills)
Overflows impacting on environment, sites of cultural significance etc
Council and expert reputation affected
Shift towards user pays, water metering and targeted rates

## Slide 45: Example: Implications arising from water quality deterioration due to increased uncontrolled wastewater discharges
Reduced resilience of waterways and environmental / habitat degradation
Reduced mental health for community members and impacting the community as a whole
Loss of cultural identity – which in turn can lead to a reduction in community cohesion and a reduction in mental health.
Exposure to poor water quality can lead to an increased incidence of disease over the short to medium term.
Reduced amenity of waterways can disrupt place-based activities in the community, which can lead to solastalgia, or a loss of sense of place
Increased preventative maintenance and water quality management costs are likely to be incurred as a response to water quality deterioration. These costs may be passed on to the community through rates and taxes, all of which may contribute to a loss of service provider reputation.
Water quality deterioration is also likely to result in a loss of tourism, resulting in medium and long term economic impact.

## Slide 46: Regional analysis

## Slide 47: Regional Analysis
How might these impacts unfold around NZ?
What type of OTHER factors may lead to lesser or greater impacts – eg demographics, socio-economic factors, infrastructure characteristics (old systems), physical situation (adjacent to rivers, coastal, floodplains, groundwater issues, droughts followed by high rainfall)

## Slide 48: Factors that may increase risk
Communities that rely on pumped stormwater systems
Communities with environmentally compromised waterways
Communities that are protected by levees/stopbanks
Focus on increased rainfall, areas of NZ that will be wetter e.g. West Coast
Communities with low-lying coastal wastewater treatment plants
Communities with WWTP which discharge to rivers
Communities with low-lying areas prone to flooding
Other factors that may mean they may have specific vulnerabilities. E.g. socio-economic

## Slide 49
Source: LGNZ

## Slide 50: Communities behind stopbanks, and expected to get wetter
Regions with townships behind stopbanks | Areas relying on pumped sw systems
Hauraki plains Lower Waikato Manawatu - Wanganui Lower Hutt Wairarapa Canterbury Otago Southland Tasman West Coast | Thames/Hauraki Plains Southland Otago (west Taieri) South Dunedin Tauranga (Papamoa) Blenheim Whakatane Palmerston North Christchurch

## Slide 51: WW treatment plant discharges

## Slide 52: Summary and next steps

## Slide 53: Confluence of issues
Climate change impacts on SW and WW
Cultural concerns around sw/ww discharges to water bodies
Ageing infrastructure
Increasing focus on receiving water quality (eg NPSFM)
Governance and institutional reform of water sector
Availability of insurance
Housing supply and land development
Notes: We need to take a systemic approach to these issues, and address them collectively
There are many related RISKS, and many related opportunities and co-benefits

## Slide 54: Guiding principles
Leadership and governance: In relation to appropriate levels of service for communities, identification and management of critical assets (based on risk), and prioritisation to those most vulnerable.
Data management, monitoring and review: Comprehensive, ongoing data capture for all env and infrastructure attributes – to enable good decisions
Technical approaches to design, asset and risk management: Climate change effects and impacts incorporated into decision making; climate risk and vulnerability well understood and adaptation plans developed.
Funding and insurance: Funding channels developed for adaptation. Insurance implications understood and monitored, intergenerational equity taken into account.
Cooperation and collaboration: Matauranga maori approaches incorporated, sharing of best practice both within and across organisations and communities

## Slide 55: Closing comments - in practice
Understand relevant climate drivers and natural hazards, what may be exposed and what risks this may present to your sw and ww networks.
Review adaptation/resilience measures that your organisation is already working on
Integrate risk assessments with asset management planning and CDEM as the base for developing CC adaptation measures.
Consider options and dynamic “pathways” which consider defend-accommodate-retreat, policy interventions, as well as hard and soft solutions, multifunctional options etc
Consider ‘what if’ scenarios with operational staff. Push the boundaries of what could happen.
Problems are complex & dynamic – we need new ways of working together to manage the climate risks we face
Greta Thunberg
Notes: Understand relevant climate drivers and natural hazards, what may be exposed and what risks this may present to infrastructure networks.
Review adaptation/resilience measures that your organisation is already working on (they may not be called climate change adaptation measures but they may be very relevant).
Integrate risk assessments with asset management planning and CDEM as the base for developing CC adaptation measures.
Consider options and pathways which consider defend-adapt-retreat, policy interventions, as well as hard and soft solutions, multifunctional etc
Consider ‘what if’ scenarios with staff. Push the boundaries of what could happen

## Slide 56
THANKYOU