## Slide 1: Source Water Risk Management Area Modelling for Groundwater: Issues and Uncertainties
Helen Rutter
Jane Alexander
Catherine Moore
16 October 2022

## Slide 2: Introduction
Background to SWRMAs
Mapping and modelling philosophy
Approaches to SWRMA delineation
Uncertainty analysis
Model and uncertainty framework

## Slide 3: Why the focus on SWRMAs?
  Havelock North and drinking water reform
  Burden of poor quality drinking water in NZ
    40-50 outbreaks per year
    34,000 NZ’ers become ill every year
  System needs to improve
    Drinking Water NES

## Slide 4: Six principles of drinking water safety
Water safety principles:
  A high standard of care should be embraced
  Protection of source water is of paramount importance
  Maintain multiple barriers to contamination
  Change precedes contamination
  Suppliers must own the safety of drinking water
  Apply a preventative risk management approach

## Slide 5: Groundwater 101
Groundwater sources tap into many different hydrogeological settings
  Springs, galleries connected to rivers, shallow wells, deep wells
Different levels of risks associated with each
  Not always simple to quantify level of risk
SWRMAs are about risk management
Many different possible approaches to delineation

## Slide 6: SWRMAs
SWRMA1 – immediate wellhead protection area
  May be a radius of between 5 and 30m
  Aim is to prevent any contamination immediately entering the well
  Strict control of land use activities
SWRMA2 – one-year travel time
  Provides time for attenuation of microbial contaminants
  Specific land use activities may be controlled
  May be no surface expression of one-year travel time
    Deep, confined aquifers
SWRMA3 – whole catchment for source
  Concern is more persistent contaminants
  May need to consider large scale discharges and cumulative effects of small scale discharges

## Slide 7: Mapping and modelling philosophy
Balance between protecting human health and maintaining productive land use
“Bad things” that we don’t want to happen
  SWRMA is too limited and people get sick
  SWRMA is too large and valuable land can’t be used or has limited use
Different SWRMA delineation approaches
Selection of SWRMA approach
  Desired level of confidence, available data, numbers supplied
For example, simple default method with demonstratively conservative uncertainty limits may be used initially
If this results in undue land use restrictions, this may be the motivation to move to a more complex model

## Slide 8: Prediction context – components influencing model approach
Number of people supplied
  Pumping rate and hence size of SWRMA
  Potentially well depth
Hydrogeological context
  Aquifer itself
  Prevalence of preferential flow paths
  Variability in conditions e.g. changes in flow gradients
Availability of data to inform model parameters
  How much can data reduce model uncertainty
  Tracer tests, age dating, aquifer tests, stream gauging

## Slide 9: Prediction context
  Simple – well is screened in homogenous, unconfined sand aquifer and is used to supply two dwellings
    Pumping rate low
    Boundary conditions can be ignored
    Model can be based on expert knowledge and site characterisation
  Complex – town supply well screened in alluvial gravels with high permeability transport pathways
    Larger pumping rate
    Will need to represent more distant boundary conditions (e.g. surface water) and how these could change over time
    Will require more complex modelling and assessment of uncertainties

## Slide 10: Approaches to SWRMA delineation
Defining the SWRMA
  Arbitrary radius/calculated radius
  Predefined shape
  Analytical modelling approaches
  Complex numerical modelling
Simple methods
Complex models
Over-large areas
More refined areas

## Slide 11: Simple approaches to SWRMA2 delineation
Arbitrary radius
  Fixed radius around the well
  Least certain, but easy and inexpensive
  2.5km radius is accepted for most aquifers
Calculated radius
  Based on abstraction, aquifer parameters and recharge
  Bases SWRMA 2 on site-specific information but doesn’t take into account flow direction
  Impacts on land use

## Slide 12: Simple approaches to SWRMA2 delineation
Predefined shape
  Dimensions depend on
    Well screen depth
    Whether confined or unconfined
  Control over
    Radius of immediate circle around source
    Up-gradient distance
For example (ECan)
  Deep well (>70m) – radius of 100m
  Shallow well (10 – 30m)
    Radius 200m
    Upgradient boundary 1000m

## Slide 13: Analytical approaches to SWRMA2 delineation
Calculate contributing area based on constant rate abstraction, flow direction and aquifer properties
Commonly a parabolic area with stagnation point down- and cross-gradient
Analytical equations used to calculate:
  Stagnation point
  One-year travel distance
  Width at up-gradient boundary
    Rules of thumb or equations

## Slide 14: Analytical approaches to SWRMA2 delineation
Input parameters include:
  Abstraction rate
  Hydraulic gradient
  Aquifer hydraulic conductivity
  Aquifer porosity
Often don’t have data but sometimes can use proxies
Lack of confidence in parameter values can be accounted for by using conservative parameters and adjusting values e.g. +/- 25%
Uncertainties in flow direction

## Slide 15: Numerical approaches to SWRMA delineation
Numerical models can be used to simulate 2D or 3D flow and transport
Accommodate more complex flow and transport
  Spatially varying aquifer parameters
  Changes between confined/unconfined conditions
  Multiple wells
  Varying pumping rates
  Boundaries e.g. rivers, no-flow boundaries
Built over larger areas and can be used to account for interference from pumping at different locations

## Slide 16: Numerical approaches to SWRMA2 delineation
May be considered where there is need to understand uncertainty clearly, or need to minimise the SWRMA extent
  Don’t have to adopt same level of conservatism as simpler models
Require good understanding of hydrogeological setting
Often not developed for SWRMA delineation but using an existing model
“Detached” SWRMAs can occur
  As can one year travel time that doesn’t arrive at the surface

## Slide 17: Approaches to uncertainty analysis
All SWRMA delineation is based on incomplete knowledge
  The SWRMA cannot be determined with certainty
As a result, uncertainty quantification is important
Uncertainty quantification describes how uncertain a prediction is

## Slide 18: Model inputs and uncertainty
Four main categories of inputs which have associated uncertainty
  Model structure – including geometry and boundaries
  Parameters – including hydraulic conductivity and effective porosity
  Stress – pumping rates and recharge
  Data – piezometric gradient and flow direction
Several approaches to uncertainty analysis
  Engineering factor of safety through to complex stochastic analyses

## Slide 19: Framework – combining modelling and uncertainty approaches
Prediction context determines appropriate approach to delineation and uncertainty analysis
Pumping rate low (small communities)
  Appropriately designed simple models with simple approach to assess uncertainty
  For example, safety margin
  Check model outputs do not contradict available data or conceptualisation

## Slide 20: Framework
Moderate to high pumping rate (large communities to cities)
  Low to moderate hydrogeological complexity
    Appropriately designed simple models
    Moderately complex methods to assess uncertainty
    History match if data is available
  High hydrogeological complexity
    More complex numerical model
    More complex uncertainty methods
    Use history matching to reduce uncertainty of capture zone

## Slide 21: Summary and discussion
Prediction context should drive approach to SWRMA2 delineation and uncertainty analysis
  Population served, hydrogeological complexity and data availability
  Uncertainty analysis needs to be considered early in the project
Simpler methods may results in larger capture zones
  A bespoke SWRMA defined by a numerical model may be better than a “default” area
Essential to have a model that is fit for purpose
  Model design may be opportunistic
  Using existing model is not necessarily best option
Time-varying nature of aquifer systems, such as potential variation (or errors) in piezometric gradient, needs to be taken into account

## Slide 22: Summary and discussion
Detached SWRMAs can occur
  Can’t be modelled using 2D approaches
  3D modelling allows this to be visualised and understood
Still investigating use of simple and “default” methods in full range of aquifer scenarios in NZ
No modelling approach will be able to 100% accurately model the one-year travel time
  Need to safeguard human health whilst avoiding unnecessary land use restrictions
  Use of appropriate models and uncertainty assessment will help to achieve this

## Slide 23
Helen Rutter
h.rutter@aqualinc.co.nz