## Slide 1: Biosolid Gasification A Case Study & Applicability to NZ

## Slide 2: Biosolid Reuse Pathways

## Slide 3: Biosolid Reuse Pathways
Landfill Disposal: $40 million/y
Operational headache + very $$
Carbon emission galore
Can’t keep filling landfill forever- tightening of consents
Environmental concerns over toxins leaching into air and water
Chart: 
| Beneficial Reuse | Landfill/Quarry Rehab
NZ | 0.16 | 0.84
Chart: 
| Beneficial Reuse | Landfill/Quarry Rehab
Australia | 0.75 | 0.25

## Slide 4: NZ low reuse reasons
Cheap
Disposal issue vs reuse potential
Negative culture perception- land application
Limited national experience in biosolid management technologies and practises
Just easier to throw it away…

## Slide 5: Development of Biosolid Gasifier at Loganholme WWTP
Operational Drivers
Loganholme is the fastest growing city within the Logan City Council (Brisbane, Australia)
350,000 EP (~ size of Christchurch)
34,000 T biosolids/year (de-watered WAS)
6 truckloads/day
300km transport for land application everyday
30% of operating costs, $1.8 million/year

## Slide 6: Drivers
Bigger Drivers
Concerns of Bioaccumulation on Agricultural Land Particularly for persistent organic pollutants (POPS)
    Europe 50% of biosolids
    AUS & NZ biosolids would also not meet these limits.
    Water industry is not prepared for this new threat to biosolids disposal.

## Slide 7: Drivers
Industry Drivers
2. Tightening of regulations: Per- and polyfluoroalkyl substances (PFAS) limits on biosolids for reuse
  Limits already applied in Queensland DES End of Waste Code for Biosolids
  Likely will be introduced in NZ in future

## Slide 8: Drivers
Internal Drivers
3. Aggressive environmental policy by Logan City Council- Net carbon zero by 2025
4 October 2020 https://www.logan.qld.gov.au/news/article/852/budget-green-is-gold-for-carbon-neutral-goal

## Slide 9: Logan Water Alliance
Let’s do something about it!..
Alliance consists of Logan City Council, Downer, WSP and Cardno (now Stantec) to collaboratively support the Council’s water goals, further improving Logan’s water and wastewater networks

## Slide 10: Many Options Considered
Process | ↓ Biosolid volume by >90% | Sterilises & eliminates odour | ↓ Metal leachability | ↓ Carbon emissions | Has end product value | End product can be stored for a long period | Destroys emerging contaminants
Anaerobic Digestion |  |  |  |  |  |  | 
Composting mix |  |  |  |  |  |  | 
Thermal drying |  |  |  |  |  |  | 
Thermal drying + pyrolysis /gasification |  |  |  |  |  |  | 

## Slide 11: Biosolid Gasification Process

## Slide 12: Biochar End Product
Stable, non-odorous, sterile
Friable, free-flowing
Easily handled and transported
Long shelf life (storage time)
Valuable reuse option

## Slide 13: Not Readily Available…
and not technically proven…

## Slide 14
1st proof concept (Downer/Pyrocal)
Concept design and technology investigations (Downer)
Concept introduced (Downer)
Part-funding sought from ARENA
$2.5M full-scale demo. Business case approved.
Final design and plant construction
Commissioning
FIRST BIOCHAR PRODUCED!!
‘17
‘16
‘18
‘19
‘20
‘21
‘22
11 Apr ‘22
Pathway Towards Commercialisation

## Slide 15: Delivery Partnership
    Downer has an exclusive technical and delivery partnership with Queensland based Pyrocal Pty Ltd
    Specialists in gasification, particularly of biomass wastes that cannot be handled by conventional technologies.
    Development commenced in 2009
    Commercial operation since 2014 with 18 units to date in 8 countries.
Technology demonstrated or operating on:
      green waste
      cotton gin trash
      rice hull, almond hull,
      sugarcane trash
      food wastes and food processing wastes (e.g. grape marc)
      animal manures, paunch waste
      biosolids

## Slide 16: Demonstration Plant (Mini Version of Full Plant)
Source 1 (dried biosolid from another wwtp in VIC)
Source 2 (dried biosolid from another wwtp in VIC)

## Slide 17: How Does it Work?- Demo Plant

## Slide 18: How Does it Work?- Demo Plant
600-650 °C. Upper rings= thermally decompose biosolids via pyrolysis (↑ temp, no oxygen)
Lower rings = inject small amount of O2 = gas-phase reaction= vaporises POPS and other gases released from the biomass to create syngas (gasification)

## Slide 19: How Does it Work?- Demo Plant

## Slide 20: How Does it Work?- Demo Plant

## Slide 21: How Does it Work?- Demo Plant

## Slide 22: How Does it Work?- Demo Plant

## Slide 23: What Was Tested For
For approval to construct the full-scale permanent plant, the demonstration plant had five key objectives
Reliability
Air emission compliance
Biosolid Biochar Characterisation (+ POPS destruction)
Heat balance
Operating Costs
  + Carbon Balance
  + Reuse Options

## Slide 24: Reliability
Reliability of mechanical, automatic and monitoring equipment
Blockages, breakages, failures
Result
Generally good
- CEMS blocked up due to moisture. Better ones will be installed in full scale plant
Test
Jan- Aug 2022

## Slide 25: Heat Balance
Test
Measure excess heat produced in water bath
Result
Source 1 = not sufficient (calories too low)
Source 2 = ok
Loganholme biosolid ~ same as source 2, so good

## Slide 26: Air Emissions
Stringent criteria were set by Queensland DES for the demonstration trial.
Test
Continuous CEMS on demo plant
Full test by independent 3rd party NATA

## Slide 27: Air Emission Compliance & Air Quality

## Slide 28: Air Emission Compliance & Air Quality
Result
Good… once runs became stable
↑ in SOx @ start-ups (~1h)
MgOH > lime for SOx control
Pelletised biosolid = ↑ dust = ↑ CO
Fresh biosolid = ↑ NOx in air
Resolved in full scale by having uniform source of biosolid, long run hours and inclusion of wet electrostatic precipitator

## Slide 29: Biosolid + Biochar Characteristics + POPS Destruction
Test Biosolid Analysis
Volatile Residue
Calorific Value
Heavy Metals
Biochar Analysis
C:N:P
Heavy metals
POPS
Microplastics
PFAS
Comparison Analysis
- Nutrients in biosolid vs biochar
Heavy metals in biosolid vs biochar
PFAS destruction
Microplastic Destruction
Carbon emissions

## Slide 30: POPS, PFAS and Micro-Plastic Destruction
Result
- 3-9 microplastic particles/g biosolid
↓60% destroyed in gasifier
- ↓ 91-100% of PFAS destroyed, all in gasifier hearth
- Improvement expected with uniform
Biosolid feed in full plant

## Slide 31: Metal Concentration & Leachability
Result
↓ ↓ Mercury and arsenic completely removed in hearth
↑ (expected) 50% increase in other metals e.g. chromium, lead and zinc however
↓ 8-10x leachability of chromium and other metals in biochar vs biosolid
Biochar chemically adsorbs much more than biosolid, new codes will factor this

## Slide 32: Consumable Operating Costs
Test
Quantify
- Power consumption
- Chemical (urea and magnesium hydroxide)
- Diesel for start-up
- No maintenance or operator costs included
Result

## Slide 33: Results- Carbon Footprint
Result
↓ 40% in 2029
↓ 20-25% through gasification process alone
Gasification sequesters 20-25% of the carbon in soil for hundreds to thousands of years
Gasification plant > transport savings for carbon emission lowering
Test
Calcs of BAU vs biosolid gasification (2029)
Carbon emissions from
Trucking/transport
Power
Carbon mineralisation of biosolid when applied to land/ landfill
Biochar chemical properties

## Slide 34: Biochar Reuse Options
2020 Bridle Consulting report
Fertiliser supplement (agriculture) - $40/tonne
Fuel, 20J/tonne - $265/tonne
Ingredient for insulating bricks and paves
Activated carbon replacement (treatment + odour control)
Metallurgic redundant
Bonus: carbon credits can be sold - $120/tonne
Logan City Council projected to earn >1$M revenue/year

## Slide 35: -Finally! Full Plant

## Slide 36: Building Construction (Oct 2021)

## Slide 37: Building Construction (Oct 2021)

## Slide 38: Solar Panels 1MW

## Slide 39: Australia’s First Commercial Biosolids Biochar
Loganholme WWTP
11th April 2022

## Slide 40: Feasibility in NZ
20,000 EP min
Tends to favour more intensified areas (Auckland, Wellington, Chch) ↑ rate base, ↑ access to skill
Places that already thermally dry sludge
Places with limited access to landfill or environmental constraints
Centralised point for many smaller communities

## Slide 41: Benefits Gained in NZ
↓ 90% biosolid volume and associated costs
↓ emerging contaminants
↓ ~100% PFAS destruction
↓ >20-25% carbon emission reduction through process alone
↑ grade, stable product with low leachbility
↑ valuable product
A real plan to tackle both biosolid management and emerging contaminants in one go.

## Slide 42: Adaptable with Existing Processes
WAS (dewatered)
Digestion (anaerobic/ dewatered)
Biochar
Drying
Gasification
Oxidisers
Existing wastewater treatment plant processes
Initially: 90 per cent reduction in transport and disposal costs.
Sources of biosolids
    Biosolids gasification can easily be designed to fit in with planned or existing wastewater operations processes.
    Gasification enables wastewater service providers to safeguard their operations against future legislative changes, cost increases with current practices, while finding new sources of revenue.
Drying
Primary sludge (dewatered)
Stockpiled sludge
Establishment of biosolids to biochar market – similar products $150 – $250 per tonne revenue

## Slide 43: Thank you
www.downergroup.com