## Slide 1: Enhanced Methane Production using an Integrated Anaerobic Digestion - Bioelectrochemical System
Afrooz Bayat
Ricardo Bello-Mendoza
Department of Civil & Natural Resources Engineering | University of Canterbury
Te Tari Pūhanga Metarahi, Rawa Taiao | Te Whare Wānanga o Waitaha

## Slide 2: Emission reduction target
Global warming is limited to 1.5˚C above pre-industrial levels.
Zero net accounting emissions of greenhouse gases in a calendar year, other than biogenic methane, by 2050.

## Slide 3: Energy use in New Zealand
In New Zealand, energy use accounts for 40% of the country’s greenhouse gas emissions.
This comprises burning fossil fuels, producing electricity, and transporting.
We can reduce those emissions by making better choices about energy use.
Source: EECA

## Slide 4: Future of fuels in New Zealand
The demand for fossil fuels must be halved by 2050.
Renewable sources of energy must be implemented for the production of heat and power (EECA and BECA, 2021).

## Slide 5: One pathway to provide renewable energy
The world biogas association (2021) highlights the capability of anaerobic digestion as a technology to:
Generate renewable energy,
Abate GHG emissions,
Contribute to meeting waste/wastewater management goals.

## Slide 6: Biogas potential and current situation in New Zealand

## Slide 7: Anaerobic Digestion
Biopolymers
(polysaccharides, proteins, lipids, etc.)
Biomonomers
(sugar, amino acids, fatty acids, etc.)
VFAs
H2, CO2
Acetic acid
CH4, CO2
Hydrolysis
Acidogenesis
Acetogenesis
Methanogenesis

## Slide 8: Biogas potential
Substrate | Biogas yield (L/kg VS) | Methane content (%)
Fat | 1000-1250 | 70-75
Protein | 600-700 | 68-73
Carbohydrate | 700-800 | 50-55

## Slide 9: Microbial Electrolysis Cells (MEC)

## Slide 10: Materials and methods
Reactor volume: 3L
Working volume: 1.5L
OLR: 0.5 gCOD/day
HRT: 30 days
Substrate strength:
10 gCOD/L
Anode: ×3 carbon felt + 0.5% pt
Cathode: ×3 carbon brush
Voltage: 0.5V
Data acquisition system
Collecting AD digestate from CWTP

## Slide 11: Results Biogas content & Daily methane production
Chart: Daily Methane Production
| 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121
AD | 194 | 194 | 194 | 224 | 194 | 194 | 194 | 219 | 227 | 194 | 185 | 194 | 194 | 194 | 210 | 194 | 194 | 194 | 194 | 171 | 193 | 170 | 193 | 193 | 164 | 164
MEC | 241 | 241 | 241 | 231 | 241 | 217 | 241 | 233 | 241 | 241 | 198 | 241 | 241 | 241 | 216 | 241 | 241 | 241 | 222 | 216 | 216 | 207 | 222 | 222 | 216 | 216

## Slide 12: Methane yield
Chart: Methane production in one cycle
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.5 | 19 | 19.5 | 20 | 20.5 | 21 | 21.5 | 22 | 22.5
AD | 0 | 0 | 15 | 31 | 46 | 62 | 77 | 85 | 92 | 106 | 118 | 124 | 131 | 139 | 147 | 154 | 154 | 162 | 162 | 170 | 170 | 178 | 178 | 178 | 178 | 178 | 185 | 185 | 185 | 185 | 185 | 185 | 193 | 193 | 193 | 193 | 193 | 193 | 193 | 193 | 193 | 201 | 201 | 201 | 201 | 201
MEC | 0 | 0 | 16 | 32 | 48 | 56 | 72 | 88 | 98 | 104 | 120 | 127 | 135 | 143 | 143 | 151 | 159 | 159 | 167 | 167 | 175 | 175 | 183 | 183 | 191 | 191 | 199 | 199 | 207 | 207 | 207 | 215 | 215 | 215 | 215 | 223 | 223 | 223 | 223 | 223 | 231 | 231 | 231 | 231 | 231 | 239
Fitted -MEC | 18.4 | 24.43 | 31.41 | 39.27 | 47.87 | 57.06 | 66.7 | 76.6 | 86.61 | 96.59 | 106.4 | 115.94 | 125.12 | 133.88 | 142.16 | 149.94 | 157.2 | 163.93 | 170.15 | 175.87 | 181.1 | 185.88 | 190.22 | 194.16 | 197.73 | 200.94 | 203.84 | 206.45 | 208.8 | 210.9 | 212.78 | 214.47 | 215.97 | 217.32 | 218.52 | 219.59 | 220.55 | 221.4 | 222.16 | 222.84 | 223.44 | 223.97 | 224.45 | 224.87 | 225.25 | 225.58
Fitted-AD | 10.73 | 16.77 | 24.47 | 33.68 | 44.12 | 55.44 | 67.25 | 79.18 | 90.9 | 102.16 | 112.76 | 122.58 | 131.54 | 139.63 | 146.86 | 153.26 | 158.89 | 163.82 | 168.1 | 171.81 | 175 | 177.76 | 180.12 | 182.14 | 183.86 | 185.33 | 186.59 | 187.65 | 188.56 | 189.33 | 189.98 | 190.54 | 191.01 | 191.41 | 191.74 | 192.03 | 192.27 | 192.48 | 192.65 | 192.8 | 192.92 | 193.03 | 193.12 | 193.19 | 193.25 | 193.31
 | P Maximum methane yield, mL | R Rate, hr-1 | L Lag phase, hour | R squared
AD | 193.6 | 23.9 | 0.19 | 0.991
MEC | 228.2 | 20.0 | - | 0.991

## Slide 13: Current in the MEC system
Chart: Current drawn from the reactors

## Slide 14: Effluent COD and VFA

## Slide 15: Conclusion
The MEC-assisted anaerobic digester had a methane production 17.5% higher than the conventional anaerobic digester.
It also showed greater process stability compared with conventional anaerobic digestion.
The performance of an anaerobic digester (i.e., substrate degradation rate, process stability, and drifting due to system upsets) can be improved with the assistance of a MEC at a voltage as low as 0.5 V.
The external energy requirement can be provided with renewable energy systems such as Microbial Fuel Cells (MFCs).

## Slide 16: Thank you !
Questions ?
afrooz.bayat@pg.canterbury.ac.nz
ricardo.bellomendoza@canterbury.ac.nz