## Slide 1
Successful R&D implementation of OdoZone odour mitigation at GV Water SHPS21
Andrew Fleming

## Slide 2
Presenter
Andrew Fleming
Senior Technical Consultant
Aquatec Fluid Systems
With over 25 years of experience in information technology, software development, analytics and R&D, Andrew leads Aquatec's innovation and product development teams. Andrew works collaboratively with clients and the wider wastewater industry towards mutually beneficial outcomes and is regularly involved in facilitating trials of new and emerging technology globally. His current major focus is on odour control systems and their efficiency gains through improved modelling and control philosophies.

## Slide 3
Odour background

## Slide 4: New challenges in Odour Control
Increasing urban encroachment on treatment facilities and their collection systems creates a number of challenges.
Quality of life issues are becoming very important for nearby residents and manifests itself in terms of odour, noise and truck traffic.

## Slide 5: Understanding Odour
Understanding the application is key to successful odour control.
Impacting Factors:
  Sources of air (headworks, liquid phase treatment, biosolids)
  Ventilation rates
  Turbulence
  Temperature
  Retention times
Need to match the treatment technology to contaminants generating the odours, as not always hydrogen sulphide.
Other components can be cause for the odour complaint
  Organic Sulphur Compounds (OSC’s)
  Volatile Organic Compounds (VOCs)

## Slide 6: H2S Removal vs Odour Removal
84.1% Removal of Total Odour
19.8% Removal of Total Odour
85% H2S
15% VOCs/OSC’s
20% H2S
80% VOCs/OSC’s
80% VOCs/OSC’s
99% removal of H2S only
99% removal of H2S only
Inlet Odour
Outlet Odour
Inlet Odour
Outlet Odour
Scenario 1: Odour mainly H2S - Residential
Scenario 2: Odour mainly VOCs/OSC’s - Industrial
15% VOCs/OSC’s

## Slide 7: Odour Overview
Historically odour control was focused on hydrogen sulphide removal, however odour is a complex mixture of chemicals.
Focusing on one only component rather than total odour can lead to failure.
Dispersion modelling is a critical part of the site evaluation of performance.
Total odour reduction becoming a key driver.
  What are the target offsite impacts: 1 OU? 5 OU?

## Slide 8
Shepparton pump station 21 (SHPS21)
Water Authority: Goulburn Valley Water

## Slide 9: SHPS21
Well Diameter: 3m
BOD: 600 mg/L
  Residential & Industrial Waste
110,000 Odour Units (OU)
  41.1% H2S, remaining other
H2S
  Avg: 14.65 ppm
  Peak: 200 ppm
Problem: Corrosion, Odour and complaints

## Slide 10: SHPS21 - location
Highly constrained site:
Public access;
On side of major roadway;
Overhead power lines; and
Commercial premises car parking and delivery receival area
Photo courtesy of Google Maps

## Slide 11: SHPS21 - location
Notes: Proximity to major roadway, power lines, and commercial premises car parking.

## Slide 12: Options Identified
Three options:
Active headspace extraction
  Biological and/or Activated carbon treatment
Chemical dosing
Oxygen and Ozone infusion
Notes: Height requirements and their proximity to high voltage overhead mains power lines
Operator activities both close to major roadway as well as high voltage overhead mains power lines
Exceeding the limited available footprint onsite
Public accessibility of the site
Visual impact
Most of the identified odour not being H2S.
  Chemical dosing at best would reduce only the H2S proportion of total odours. i.e. 41.1%

## Slide 13
Trialling oxygen and ozone dosing at SHPS21

## Slide 14: Trial unit
The trial unit, pump, infuser and gas lines installation
Notes: In its first week, the baselined H2S levels were captured for later comparison, and in the second week, different dosing set points were trialled to gauge H2S removal effectiveness.
The effect of dosing Oxygen and Ozone on H2S levels was noticeable immediately.

## Slide 15: SHPS21
Dosing results
Not Dosing
Peak H2S: 48.2 ppm
Average H2S: 14.3 ppm
System turned off demonstrating effect without dosing
Dosing 60/20
Peak H2S: 7.9 ppm
Average H2S: 0.15 ppm
Reduction: 99%

## Slide 16: SHPS21
Odour Profile & removal efficiency
Other
OU: 5,800
100%
Other
OU: 64,787
58.9%
H2S
OU: 45,213
(21.25ppm)
41.1%
H2S
OU: 0
(0ppm)
0%
Not dosing
  110,000 Odour units
  H2S 21.25ppm
Dosing
  5,800 Odour units
  H2S 0ppm
Odour Removal Efficiency
  100% H2S removal
  91.0% Other (non H2S) Odour removal
  94.7% Total Odour removal
Notes: GVW expanded the trial’s parameters for removal of other contaminants, and to assess the effect on downstream odour prevention.
For the subsequent two weeks, the unit was tested against non-H2S odours, and its effect on the rising main which discharged six kilometres away at SHPS5 was assessed.

## Slide 17: Downstream Effect
SHPS21 discharges through a common rising main to SHPS5.
Rising main details:
Length: 6,000 meter
Avg Diameter: 375mm
Avg Detention time: 2-3 hours
Air valves installed: Yes
SHPS21 – Dosing location
SHPS5 – Discharge location
Map courtesy of Google Maps

## Slide 18: Downstream Effect
Hourly Average H2S at SHPS5
Not Dosing
Peak H2S: 597 ppm
Average H2S: 53.6 ppm
System turned on demonstrating effect downstream
Dosing 60/20
Peak H2S: 47 ppm
Average H2S: 4.5 ppm
Reduction: 91.6%
Notes: SHPS21:
H2S Avg: 14.65 ppm
H2S Peak: 200 ppm

## Slide 19: TOTEX comparison
Notes: Whilst chemical dosing was determined to be a non-viable solution, a TOTEX comparison between it and ozone dosing for the first 60 months was calculated. It showed an ROI (return on investment) of 13 months when compared to chemical dosing.

## Slide 20
OdoZone

## Slide 21: Odour and Corrosion Control
The OdoZone is designed for FOG, odour & corrosion control within the wet well.
It works by drawing in ambient air from the environment to generate an Oxygen/Ozone mixture.
A grinder pump recirculates treated wastewater from the wet well through the BETE nozzle, which then showers it back throughout the wet well.

## Slide 22: Sewer Sulphide Cycle
Bacteria in wastewater collection systems will use (in order of preference) dissolved oxygen, nitrate, and sulphate as oxygen sources for respiration.
Dissolved oxygen is usually present in fresh wastewater, but is rapidly depleted by biological activity within the first couple of hours.
There is typically very little nitrate present in the wastewater, while sulphate is typically abundant. Since little or no nitrate is available, the bacteria begin utilising sulphate when the dissolved oxygen is depleted.
The by-product of the sulphate uptake process is dissolved sulphide. The dissolved sulphide combines with hydrogen ions to then form odorous Hydrogen sulphide. In combination with creating odours, Hydrogen sulphide can also be oxidised creating Sulphuric acid, causing corrosion problems in downstream assets.

## Slide 23: About Ozone
Very high oxidation/reduction potential @ 2.07V
      Hydrogen peroxide (1.77V)
      Chlorine (1.36V)
      Oxygen (1.23V)
Has a half-life of up to 30 minutes in water
Has a half-life of seconds to minutes in wastewater
Ozone- very wide range of reactions
  Sulphides, sulphur compounds
  Ammonia: 2NH3 + 3O3  N2 + 3H2O + 3O2
  Organic compounds including solids & VOCs
  Pharmaceuticals, petroleum byproducts, and colour/dye removal
Ozone is 13x more soluble than oxygen
Degrades to oxygen (O2) upon reaction with sulphides
H2S
H2O
SO2
O3
O2
SO3=
SO4
O3
O2
O3
Notes: H2S - Hydrogen Sulphide; SO2 - Sulfur dioxide; SO3= - Sulfite; SO4 – Sulfate;

## Slide 24: How It Works
The dissolved ozone instantaneously begins to reduce and oxidise any H2S into non-odorous sulphate.
While the treated wastewater recirculates in the wet well, it continually mixes with and treats new wastewater.
The increase in dissolved oxygen generates aerobic activity over Anaerobic Bacteria, reducing H2S downstream and eliminating the potential for Sulphuric acid and associated corrosion issues.
Notes: Resets the clock
Breaks the chain to Sulfuric Acid

## Slide 25: Ideal Application
Upstream odour issues, causing complaint and corrosion at residential pump station.
Footprint limitations onsite
Targeting not just H2S
Relative short detention time in downstream rising main (hours not days).
  As with SHPS21

## Slide 26: Typical OdoZone Footprint
Notes: No bunded area, truck parking, tanks, sheds, spill kits, safety showers, etc

## Slide 27: Conclusion
Reduction in odour onsite at SHPS21, and expected complaint levels
Minimising ongoing corrosion at SHPS21
Reduction of expected complaint levels at air valves along rising main.
Reduction in odour and corrosion levels at receival point (SHPS5)
Reduced Operational costs in comparison to traditional chemical dosing
Notes: Oxygen and Ozone injection into the wastewater at SHPS21 was successfully trialed to determine its effectiveness in reducing the odours both at the pump station, along with the downstream rising main and receiving pump station.
Permanent OdoZone system as shown in the image

## Slide 28: Questions

## Slide 29
Presenter
Andrew Fleming
Senior Technical Consultant
Aquatec Fluid Systems
M: +61 437 890 322
E: afleming@aquatecenviro.com
NZ 0800 756 543
AU 1300 088 555
Stands: 179, 180, 185, 186