## Slide 1
FEASIBILITY STUDY
USING TREATED WASTEWATER FROM MANGERE AND ROSEDALE WWTPS FOR SPORTS-FIELDS IRRIGATION IN AUCKLAND
SARISHA HURRISUNKER

## Slide 2
NZ Context
Cultural Significance to Māori
International Guidelines
Effluent Data Analysis and Results
Environmental and Public Health Risks
Next Steps
OUTLINE

## Slide 3
DROUGHT
AUCKLAND’S DROUGHT MOST EXTREME IN MODERN TIMES
NIWA 22 MAY 2020

## Slide 4
AUCKLAND COUNCIL'S COMMITMENT TO REDUCE WATER CONSUMPTION
-30% BY 2030

## Slide 5
Community Facilities
Average Water Use
Auckland Council
Irrigation
45%
Buildings
18%
Aquatic Centres
15%
Toilets & Change Rooms
14%
Community Halls
5%

## Slide 6
NEW ZEALAND
Mercury Bay Sports Field
THAMES COROMANDEL
Omaha Beach Golf Course (OBGC)
Jones Road Sites (JRS) - Eucalyptus and Native Plants
OMAHA
193ha Whakarewarewa Forest Scheme
ROTORUA
LAND BASED DISCHARGE SCHEMES

## Slide 7
"Ko te wai te ora ngā mea katoa"
Water is the life giver of all things

## Slide 8
 | USEPA | AGWR CLASS A | NSW
PH | 6 - 9 | - | 6.5 - 8.5
BOD (mg/L) | < 10 | < 20 | < 20
Turbidity (NTU) | ≤ 20 | ≤ 20 | ≤ 20
Residual Chlorine (mg/L residual) | 1 | 1 | 1
Faecal Coliforms (FC/100ml) | No Detectable | - | -
Escherichia (E-coli/100ml) | - | < 10 | < 10
International Guidelines

## Slide 9
MANGERE
WWTP

## Slide 10
ROSEDALE
WWTP

## Slide 11
Mangere WWTP
CMAS + MLE
Rosedale WWTP
MLE

## Slide 12
Effluent Data
Analysis & Results
Samples 12 August 2021
Results 2 September 2021
TEST DATA
22 July 2016 to 21 July 2021
HISTORICAL RECORDS
Historical Records
Test Data
DATA SOURCE

## Slide 13
 | MANGERE | ROSEDALE | NSW
BOD (mg/L) | 2.4 - 4 | 0.8 - 1.5 | < 20
Total Nitrogen (TN) mg/L | 7.7 - 9.5 | 8.2 - 9.9 | 5 - 50
Total Phosphorus (TP) mg/L | 2.3 - 2.8 | 2.7 - 3.2 | 0.5 - 10
pH | 7.2 - 7.4 | 7.2 - 7.9 | 6.5 - 8.5
Total Dissolved Solids (TDS) mg/L | 480 | 450 | 600 - 1000
GENERAL CHRACTERISTICS

## Slide 14
 | MANGERE | ROSEDALE
Faecal Coliforms (cfu/100ml) | 31 | 11.2 - 301
Enterococci (cfu/100ml) | < 1.6 | 40 - 70
PATHOGENS
Collect and Analyze additional data
Review existing process performance and optimisation
Identify opportunities for additional treatment controls
MITIGATION MEASURES

## Slide 15
 | MANGERE | ROSEDALE | NSW
Electrical Conductivity (dS/m-1) | 0.545 | 0.545 | 0.65 – 1.3
Sodium Adsorption Ratio | 4.9 | 4.5 | 10 – 18
SALINITY

## Slide 16
 | MANGERE | ROSEDALE | NSW
Arsenic (As) mg/L | 0.0017 | 0.0018 | 0.1
Cadmium (Cd) mg/L | <0.00005 | 0.000221 | 0.01
Copper (Cu) mg/L | 0.0015 | 0.0035 | 0.2
Iron (Fe) mg/L | 0.058 | 0.099 | 0.2
Lead (Pb) mg/L | 0.00028 | 0.000439 | 2.0
Manganese (Mn) mg/L | 0.065 | 0.038 | 0.2
Nickel (Ni) mg/L | 0.0078 | 0.00365 | 0.2
Zinc (Zn) mg/L | 0.051 | 0.02975 | 2.0
HEAVY METALS

## Slide 17
 | MANGERE | ROSEDALE | METHOD DETECTION LIMIT
Diuron μg/L | 0.3 | 0.7 | 0.1
Terbuthylazine μg/L | 0.3 | 4.2 | 0.1
Mecoprop (MCPP) mg/L | 0.00015 | 0.00051 | 0.00010
Triclopyr mg/L | 0.00012 | 0.00043 | 0.00010
TRACE ORGANIC COMPOUNDS

## Slide 18
ENVIRONMENTAL EFFECTS
Presentations are communication tools that can be demonstrations.
RAISE AWARENESS IN COMMUNITY.
Presentations are communication tools that can be demonstrations.
GROUNDAWATER
CONTAMINATION
Pathogens
Nitrate
Emerging Contaminants (PFAS)
SOIL
HEALTH
Salinity
Heavy Metal Accumulation
Pesticides, Herbicides
Nitrogen, Phosphorus Toxicity

## Slide 19
PUBLIC HEALTH RISKS
Presentations are communication tools that can be demonstrations.
RAISE AWARENESS IN COMMUNITY.
Presentations are communication tools that can be demonstrations.
MITIGATION
MEASURES
Drip Irrigation System
and
Operational Protocols
DIRECT EXPOSURE TO PATHOGENS, TOXIC CHEMICALS AND EMERGING CONTAMINANTS

## Slide 20
NEXT STEPS
NATIONAL RECYCLED WATER REUSE GUIDELINES
MĀORI ENGAGEMENT
Te mana o te wai
Te mauri o te wai
PILOT PROJECT
Progress pilot project at Rosedale WWTP

## Slide 21
Thank You