## Slide 1
ASSESSING THE REAL-WORLD BENEFITS OF SOLAR PV FOR WATER UTILITIES
POWERING A GREENER FUTURE
Water New Zealand Conference & Expo - 2022
Damien Dupont – Green Energy Specialist
Notes: Good morning everyone and thx intro
I’m here today to talk about Solar PV TECH, especially for W.U
Before I start, I'd like to acknowledge my predecessor
We’re gonna try to answer a question today : Can solar help W.U to power a greener future

## Slide 2
Context
Why Solar ?
Case Studies and Results
The Future
Notes: How Approach
Firstly – I’ll start by giving you the context (climate change + electricity)
Then, case for Solar PV and why see it solution
Interesting part : Already done some projects - used them as Case Studies – have Results to present
These results encouraged us to pursue our solar journey – that’s why I’ll present in the conlusion

## Slide 3
Context : Climate Change…
Main cause : GHG emission from human activities
Warming : expected max + 3°C by 2100
Considerable challenges for the Water
and Wastewater Industry
Growing Frequency : extreme weather, dry periods, rising sea levels
Requires immediate and significant action
50% operational emissions reduction by 2030
Net Zero emissions and energy use by 2050
Energy Neutral at major WWTPs by 2030
Notes: Start 2 key contexts
Talked last few years - not new for anyone – predictions
Will be multiples consequences if not act urgently
Unfortunately for us, W.U are amongst most impacted
Dry periods - extreme weather events - sourcing water from distant – energy intensive
WSL has set targets and commitments

## Slide 4
Context : Electricity constraint…
Significant Emissions Source & Operational Cost = Opportunities to explore more renewables
20% increase in 3 years
Notes: In NZ, Indus processes + energy use in top 3 factors GHG
Almost 60% of our emissions… ELECTRICITY 1st
20/21 200GWH : 20% + than 17/18
PB : Aging Infra – maintenance – pop growth more demanding -- ENERGY INTENSIVE
If we add the estimations giving a rise in electricity prices -- Urgent for WATERCARE
Need solution to mitigate financial and enviro impact : USE ENERGY FROM MORE RENEWABLE SOURCES

## Slide 5
Solar P.V…
Major lever to control our emissions
and meet our climate action targets
Renewable energy tops the list of changes
the world can implement to tackle
Climate Change
Improvement in solar generation technology
Cost : 70% less in just 10 years
Increasing returns from marginal land
Certainty of fixed costs for ≈ 25 Years
Low maintenance
Notes: We see 2 main problems : Climate & Electricity
Luckily there’s a solution – getting our energy from more renewables sources
Watercare unique position (Biogas Cogen + Hydropower) - Not enough… What complement ?
Solar PV - Key component in renewable energy Mix
Cheapest form - easy install / quickly – reliable – low maintenance – doesn’t produce carbon emissions
Last 10 years – TECH improved – Cheaper = (Widely available + Affordable)
WHAT DO WE WANT : reduce opex cost – reduce carbon emissions - hedge

## Slide 6
Since 2019 : Pilots projects & Floating array at Rosedale…
Pukekohe 122kW
Redoubt Rd 142kW & 225kWh
Rosedale 1,040kW
Wellsford 65kW
Notes: With that in mind: Watercare Business case 2018
Develop understanding PV tech – test supply market capability
Arrays completed in 2019
Successful so bigger scale – the result was the Rosedale Array
We can now share observations and lessons to assist other W.U
Today, going to take 3 projects case studies
Explain what was our approach – expectations - high lvl outcome

## Slide 7
Case Study : Pukekohe WWTP
Reduce Grid Import : Expected Benefits
  January 2019
  122kW ground mounted array
  168.000 kWh p.a
  Reduction of grid import : 20%
  Opex Cost Savings : $20,350 p.a
  CO2 emissions reduction : 19T p.a
Notes: Pukekohe WWTP
122 kW ground
Goal : Reduce grid import and opex cost savings
Expected to : reduce 20% import – Opex -20.000$ - 19T CO2 reduction
Key metric : to this date – a bit less than 1% - GOOD FOR 1st project

## Slide 8
Case Study : Redoubt Rd Reservoir
Resilience focus : Expected Benefits
  July 2019
  142kW array + 225kWh
  196.000 kWh forecast p.a
  Reduction of grid import : 76%
  Battery - 6 hours endurance - 1.5 hours in reserve
  Opex Cost Savings : $18,300 p.a
  CO2 emissions reduction : 12.9T p.a
Notes: Strategically important asset
Up 2/3 of treated water supply each day
Main goal was about Resilience
142kW roof mounted array, coupled 225 kwh Tesla battery pack
Expectations : 76% reduce grid – 6h/1h30 reserve – Opex 18.000 – 13T reduction CO2
Output more than the forecast 0.86%
These 2 projects achieved their objectives and expected benefits
Encouraged us to build at a bigger scale.

## Slide 9
At a bigger Scale…
Neutral at our Major WWTP by 2030
2nd largest WWTP in N.Z
Cogen already up to 80% of Energy
T.O.U site : Half-Hourly metered data
Use of Marginal Land
Close to 11kV ring main
Not interfering with Operations
Better economy of scale
Notes: In important point to know is : Solar has strong economy of scale
Also a reason to go bigger
Now, Why Rosedale ? target 2030 – 75% Cogen – T.O.U = good understanding of energy profile
Another benefit I haven’t mentioned yet : Marginal land
Ticked all the boxes : innovative solution floating

## Slide 10
1st Floating Solar Array in N.Z
2700 Solar Panels
≈ 4000 floating pontoons
9,500 m2 total surface
Assembled in 4 sections
65 x 2,4 tonnes anchor points
16 Inverters : 1MW DC to 800kW AC
Transformer to step up to 11kV
Notes: Summarise
End 2020

## Slide 11
Case Study : Rosedale 1mW Floating Solar Array
Commitment focus: Expected Benefits
  October 2020
  1MW floating array
  1.47 GWh forecast p.a
  Max reduction of grid import
  Opex Cost Savings : $127.000 p.a
  CO2 emissions reduction : 145T p.a
Notes: Same approach
Expectations : 127.000 $ pa – 145T pa – bring energy neutrality
-1.7 % - different factors – scale impacting more results between forecast and annual - mostly maintenance
-1.7% is still close – for project this scale and for being the 1st floating – we consider it success – still all benefits

## Slide 12
Summary of Watercare achievements
  Reduce grid import by 3.9 GWh = Energy consumption of 536 NZ homes for a year
  Reduce CO2 emissions by 394 Tonnes
  Improve resilience of our installations
  Opex cost savings estimated at : $ 468,000
  Achieve energy neutrality at one key site
Notes: So far Solar journey success, especially for our very first projects
3 Completed projects : met expectations – also brough experience and confidence to see bigger for the next years
Summary : (-3.9Gwh + 536 Homes) – 394T reduction + improved resilience +Rosedale Neutral + 468k Opex Saved

## Slide 13
The Future
  10 Projects to 2030 –up to 50MW Solar PV
  Up to $ 7 Millions Opex Savings p.a
  Emissions reductions of 6,000t CO2e p.a (MfE)
  Reduce Grid Import by ~ 30% (60GWh)
  Half of our 50% operational emission reduction target (Electricity Part)
Notes: All results were encouraging
Led to creation of Solar Rollout Programme (G.E.S)
10 additional projects – up to 50MW Solar on WSL land
Estimated reduction grid import 30%
For an Investment of 70 Million, we forecast a 7 Millions Opex cost saving p.a
Reduction of Co2 6000T p.a
Certainty of fixed cost for 25/30 years
Finally, it will help to reach the target to reduce by 50% Ops emission elec

## Slide 14
A proven, key part of efforts to reduce energy emissions
Conclusion
The business case for solar PV at Water Utilities is strong and diverse
Delivers opex cost savings + hedge against energy price rises
Improves resilience of critical assets
Generates revenue from marginal lands
Improves our social license to operate
Enhanced public perception
Notes: Due to availability and price decline in last 10 years
Solar PV most accessible and affordable distributed energy solution
Water Utilities have now opportunity - strategic objectives
Especially because, Energy is the 1st lever we can use to reduce Ops cost + Reduce GHG
Business case MULTI FACETED – Repeat myself (Reduce Emissions + Opex Savings/Hedge + Resilience + Marginal Lands + Public)
Help W.U global fight – progress towards goals adopted U.N 2030 Agenda
Also, as we embrace an Era of Water Sector reform – we can have confidence not choosing (enviro – energy security – sound economics) to become successful utility future
Does Solar PV ??? YES

## Slide 15
ASSESSING THE REAL-WORLD BENEFITS OF SOLAR PV FOR WATER UTILITIES
POWERING A GREENER FUTURE
THANK YOU
Damien Dupont – Green Energy Specialist