## Slide 1
Water Conference NZ
Pipe Alignment Tool: Optimising Servicing Strategies for Unconnected Properties
Andrew Liese BE(Hons) Computer Systems

## Slide 2: Background
Yarra Valley Water
7,000 high risk properties to be connected into the network.
Many More “Low Risk”
6 Weeks
Automated Approach?
Notes: Who are YVW
YVW Pricing Submission Requirements
Project Scope
They own and manage over 20,000 kilometres of water and sewer mains, servicing over 2 million people.

## Slide 3
Notes: Who are YVW
YVW Pricing Submission Requirements
Project Scope
They own and manage over 20,000 kilometres of water and sewer mains, servicing over 2 million people.

## Slide 4: Automated Approach?
Replicate Detailed Traditional Approach
  Replication of Engineering Judgement
Replicate a couple of broad strokes?
  Building center points as connections
  Follow Road

## Slide 5: Automated Approach?

## Slide 6: Lessons Learnt
Network Constraints
  Gravity
  Pressure
  Rising Main
Parcel Low points
  Overall For Gravity
  Building Adjacent for pressure
Soil Types
Cost

## Slide 7: Haves and Have Nots
We Have | Don’t Have
Parcels – with risk values | Detailed LiDAR
Roads Layer (OSM) | Soil Composition
Existing Sewer Nodes | Cost Tables
Building Footprints | 

## Slide 8: Ground Conditions
VicMap Geology layer GEOL250
Granite
Siltstone
Clay

## Slide 9: LiDAR Availability

## Slide 10: Methodology
Overview
Roads as Potential Pipes
Shortest Path
Each segment has 2 pipes
Improvements
Gravity flows downhill
Assign Cost
Add Pressure and RM
Connect Gravity to RM
Allow ‘Dig Deeper’ Method

## Slide 11
Upstream
Downstream
Higher
Elevation
Lower
Elevation

## Slide 12: Outcome / Delivery
Wins!
Last Minute Scope Change
All High Risk Properties Connected
Around 3.5k Low Risk as well
Pipe Sizing
Model Compatible
But….
RM Pump Station Placement
Booster Station placement
5% - 10% Manual Work
Still Mostly Pressure

## Slide 13
Pressure networks into gravity networks
Gravity into Pumping Station into Rising Main
Pressure and rising main in same street
Pressure network flows back towards pumping station
Rising main flow direction

## Slide 14: Future Work
Already re-used in NZ and Australia
Ongoing developments for scenario comparisons
Same Client came back with expanded scope
Refining to better reflect Engineered Solution

## Slide 15: Questions?

## Slide 16
Without change there is no innovation, creativity, or incentive for improvement. Those who initiate change will have a better opportunity to manage the change that is inevitable.
William Pollard

## Slide 17: Extra For Experts