## Slide 1
Challenging the Status Quo
An Innovative Approach to Structural
Renewal of a Large Box Culvert
Marc Ciochetto & Cory Higgins
Notes: Kia Ora, thank you XXX for that introduction, at Interflow we like to challenge the status quo in our quest to solve customers problems and today, Marc and I will be presenting a case study of a project where we did just that

## Slide 2
Agenda
Project Background
Considered Renewal Options
Channeline Overview
Design & Construction
Project Outcomes
Notes: During a culvert inspection program in 2020, the culvert you see behind me was identified as requiring urgent renewal by Sunshine Coast Council’s Stormwater Asset Management team. The reason we are presenting a case study of a project in Australia is simply, that this system has never been used in New Zealand and we thought it was something worth sharing with you.
Todays presentation will cover
The background of this project,
Considered renewal options,
An overview of the Channeline product which was our Chosen renewal option
Site Construction
and the project outcomes

## Slide 3: Project Background
Notes: So, the project background

## Slide 4
Project Location
Amarina Ave, Mooloolaba, Queensland
Notes: Constructed in 1975, the culvert passes under a busy street, taking run-off from the Motorway and into a Canal.

## Slide 5
Site Conditions
Culvert located under the roadway
District collector with 2 traffic lanes signed at 60km/hr
Carriageway is 12.8m wide, 2 x 3.2m lanes and shoulder either side.
Bus stop and shelter on either side.
Culvert takes catchment from the Sunshine motorway, is tidal influenced and connects to the Mooloolaba Canal
North Bound Approach
South Bound Approach
Notes: The road under which the culvert runs has a 60Km/h speed limit, 2 traffic lanes, with a shoulder either side.
A bus stop shelter in each direction and a pay phone both for good measure
Culvert takes catchment from the motorway, is tidal influenced and connects to a Canal

## Slide 6
Existing Culvert Structure
Constructed: 1975
Dimensions: H2.1m x W2.1m
Length: 36m
Split into 3 Sections:
Unit 1 – Cast Insitu 18.2m
Unit 2 – Precast 1.3m
Unit 3 – Cast Insitu 16.6m
Notes: The existing structure is cast insitu reinforced concrete construction with internal dimensions of 2.1m high x 2.1m wide, and length of approx.. 36m
At some stage an internal repair had been completed using a precast concrete section of approx. 1.3m
The haunches and wall thickness of this precast section reduced the internal dimensions at this point, as seen in the photo.

## Slide 7
Culvert Inlet
Inlet Structure – East Towards Canal
Water Way Inlet Side – West, Towards Sunshine Coast Motorway
Notes: The culvert inlet is located on the western side of the road in a small park, containing mature trees which backs onto a Motorway
The depth of cover over the structure is approx. 2m

## Slide 8
Culvert Outlet
Outlet Structure – Into Canal
Water Way Outlet Side – Into Canal
Notes: The culvert outlet is located on the eastern side of the road, also in a small park, and runs into the Canal.
There are several large mature native trees located directly over and close to the culvert alignment on this side

## Slide 9
Culvert Condition
Notes: Routine inspection of the this culvert showed that action was required.
Obvious deterioration, particularly the section closest to the outlet end, caused concern about the possibility of collapse.
Their report found extensive spalling and corrosion to reinforcement.
Culvert replacement was recommended, with culvert lining also considered as a rapid and potentially cost-effective solution.
The most severely affected areas were immediately barricaded at surface level to prevent heavy vehicle loads.

## Slide 10: Renewal Options
Notes: Renewal options, listen carefully as I will test you on this later!

## Slide 11
Renewal Options – A, B & C
Notes: An analysis of possible options was undertaken. The options evaluated were:
Option A - Slip lining new box culvert sections inside the existing culvert, sitting on a new base slab laid over the existing base
Option B - Slip lining with a 1500mm diameter polyethylene pipe encased in flowable fill over a new base slab
Option C - Excavation and removal of the roof, then installation of a higher box culvert to reduce flow area loss.

## Slide 12
Renewal Options – D, E & F
Notes: Option D - Excavation and replacement of the roof slab, repair of the walls, plus a new base slab
Option E - Excavation, then replacement of the culvert on a new reinforced concrete base slab
Option F - Installation of supplementary roof and base slabs under and over the existing slabs

## Slide 13
Design Considerations
Decay of Existing Structure
Cross Sectional Area Loss
Flood Modelling
Geo Tech
Existing Underground Services
Notes: Flood modelling showed that majority of these options caused a major reduction in flow capacity, so were not viable.
The options that were ‘acceptable’ required
  extensive excavation,
  lengthy road closures,
  and the relocation of telecommunication services, electrical conduits, and a water main which all crossed the culvert.

## Slide 14
Environmental Considerations
Coastal Management District
Acid Sulphate Soils (AHD between 1 to 5M)
Aboriginal Cultural Heritage Duty of Care
Disturbing of Marine Plants
Tidal Water
Erosion and Sediment Control
Tree Removal
Notes: Council’s initial assessment concluded that the most practical was excavation of part of the culvert and replacement of its roof, with repair work to the remainder of the structure
As well as the environmental risk of run-off from excavated material, this procedure had the potential to trigger environmental requirements for the disruption of acid sulphate soils and the disturbance of marine plants.
Additional controls would be required adding further cost and time to this project.
In addition, the dig and replace method would require the removal of several large native trees; on or over the culvert alignment.

## Slide 15
Alternative Solution: Channeline
Notes: The Interflow team looked at an alternative solution using Channeline to structurally renew this culvert.
we had used Channeline on similar projects and this approach was to slip line the culvert with structural GRP profile segments, custom made by Channeline to maximise the culvert existing dimensions.
I will now hand over to Marc to give us an overview of the Channeline technology.

## Slide 16: Channeline Overview

## Slide 17
About Channeline International
Developed in 1984 in UK
Custom Built, Bespoke Structural GRP Lining System
Liners have been installed in over 30 countries worldwide
Notes: Developed in 1984 in UK
Custom Built, Bespoke Structural GRP Lining System
Liners have been installed in over 30 countries worldwide.

## Slide 18
What is Channeline?
Channeline is a Glass Reinforced Plastic (GRP) or Fiber Reinforced Polymer (FRP) Grouted In Place Panel Lining System.
Any Shape, Size or Profile
Can be utilized to structurally rehabilitate any Host Pipe Material
Notes: Channeline is a Glass Reinforced Plastic (GRP) or Fiber Reinforced Polymer (FRP) Grouted In Place Panel Lining System.
Any Shape, Size or Profile
Can be utilized to structurally rehabilitate any Host Pipe Material

## Slide 19
What is Channeline?
GRP Sandwich Composite I-Beam Construction:
Inner corrosion barrier consists of 1.5mm (0.6”) of Isophalthalic, vinylester or epoxy resin. Can also be designed with superior Abrasion Resistant material
Consolidated, bi-direction fibreglass mat and resin
Center core consists of silica sand and resin
Second layer of fibreglass mat and resin
Outside surface is treated with bonded aggregate to enhance adhesion with grout
The result is a flexible but structural liner that will resist live loads, dead loads and hydrostatic pressure
COMPRESSION
TENSION
Notes: Channeline’s construction is an I-Beam GRP Sandwich Composite.
The Result of the i-Beam Construction is a flexible but structural liner that will resist live loads, dead loads and hydrostatic pressure.

## Slide 20
Why GRP?
Proven Track Record – 38 years of history with no known failures
350 Plus Projects completed in North America over a 20 year period
Liner can be custom built to fit through existing access shafts
Fully Structural 100 Year Design
Leak tight Jointing System (Tested and Certified)
Productive and Low Tech Installation
Local Representation and Technical Support
21 years of experience
Notes: Why GRP
Proven Track Record – 38 years of history with no known failures
350 Plus Projects completed World Wide over a 20 year period.
The Liner can be custom built to fit through existing access shafts and Manholes
Fully Structural with a 100 Year Design life Including a Tested and Certified Leak tight Jointing System
With a Low Tech Installation method achieving high On Site Productivity.
Including Local Representation and Technical Support World Wide

## Slide 21
Why GRP?
Hydraulic Capacity:
Channeline will give an improvement to the flow capacity and hydraulic self-cleaning ability between 12% and 20% typically using Manning coefficient value of “n” 0.009.
In some environmentally sensitive areas such as Fish Bearing creeks, it is necessary to slow down the flow. This can be done by applying a non-slip surface to the liner invert.
Notes: Hydraulic Capacity
Channeline will give an improvement to the flow capacity and hydraulic self-cleaning ability, typically between 12% and 20%
In some environmentally sensitive areas such as Fish Bearing creeks, it is necessary to slow down the flow.
This can be done by applying a non-slip surface to the liner invert or by installing Fish Baffles.

## Slide 22
Why GRP?
GRP Panels are supplied with a socket and spigot joint with is used in conjunction with a gasket or construction sealant.
GRP two piece and multi-piece lining units come with a tapered tongue and groove longitudinal joint and a bell and spigot radial joint.
Joints using Solid Rubber Gaskets are regularly tested in accordance with ASTM D 4161 to 2.2 bar (33.359 psi)
However, Channeline have successfully performed modified gasket joint tests (no reference standard available) to 15 bar (217.56 psi)
Notes: GRP Panels are supplied with a socket and spigot joint which is used in conjunction with a gasket or construction sealant.
GRP two piece and multi-piece lining units come with a tapered tongue and groove including a longitudinal joint and a bell and spigot radial joint .

## Slide 23
Why GRP?
Fully Customizable sizing – no off the shelf moulds
In House Research and Development Department
In House Testing and Compliance Laboratories
Tangible Lining system, manufactured under
Strict QA/QC Protocols (not cured/built in place)
Low Tech Easy Installation
Low Carbon Footprint Construction
10 Year Materials Warranty
High Mechanical Properties for Design purposes​
Long Term Flexural Modulus 4,000Mpa
Hydraulic Performance​ “n” 0.009, “K” 0.03
Design life of 100 years Compliant with ASTM D3262,
ISO 16611 and WIS 4-34-02
Notes: Fully Customizable – No Design is the same, every project is of a different diameter and shape,
Channeline build to the internal diameter of the host pipe,
Segment lengths from 200mm to 2.4 meters in length (MSI)
Channeline have an in House Research and Development Department including Testing and Compliance Lab
Lining system, manufactured under Strict QA/QC Protocols
Construction has a Low Carbon Footprint
High Mechanical Properties with a design life of 100 years and a 10 year Materials Warranty

## Slide 24
Design
AS5100 Bridge Design Code
AS1170 Structural Design Actions
AS3571 Plastic Piping System GRP
Water Research Centre – Sewer Rehabilitation Manual
TMR’s Bridge Design Criteria & Other Structures
Notes: Channeline generated the profile geometry and initial liner design
The design is for standalone structural requirements.
Profile wall thickness of 64mm was required for this project.
The external dimensions of 2mx2m of the Channeline profile allowed for a 50mm annular gap to aid installation into the culvert.
A flood model was then run with the proposed Channeline profile.
This scenario was found to have minimal impacts on the majority of local flood events.

## Slide 25
Design Submission
Design developed from first principles by SASTTI JV, Sewer Assessment & Trenchless Technology Specialist Consulting Engineers
Finite element model created
Notes: Interflow engaged external consultant to check the design
Finite Element (FE) analysis was conducted from first principles to confirm design was suitable.
The results of the analysis confirmed that a “Channeline” lining profile with a wall thickness of 64mm has sufficient structural capacity to meet the renewal objectives.

## Slide 26: Construction
Notes: I will now hand back to Cory to talk through the site construction

## Slide 27
Project Award
D&C Contract awarded to Interflow who provided:​
Innovative design using Channeline meeting all the mandatory design criteria​
Construction methodology that limited the risk of environmental harm
Short construction duration minimising impact to traffic​
Notes: Channeline was accepted as the preferred renewal solution, due to benefits of cost, enviro impact and reduction in community disruption

## Slide 28
Site Setup
Isolation of Outlet Structure & Installation of Double Silt Curtains
Isolation of Inlet Structure
Temporary Staircase at Inlet Side of Culvert
Notes: Before installation works could commence, the site required isolation of the tidal canal and work areas.
The bus stops were temporarily moved south of the works area to provide safe access for the local community
A temporary stair case was constructed at the inlet end of the culvert as the main entry and exit point to the culvert

## Slide 29
Coffer Dam
Notes: The culvert is subject to tidal inflow from the canal.
As dry working conditions were needed, one of the first tasks was to construct a coffer dam at the outlet end.
Typically sheet piling would be used, but we were able to source a Swedish designed system which uses interconnected, extendable sections to provide a robust temporary barrier system.
A coffer dam 5 metres wide and 2.4 metres in height was rapidly constructed.
Water in the culvert was pumped over the coffer dam to create a dry workplace.
Outside of the coffer dam a double bund was installed.
The bund barriers, placed in parallel with a gap between them, had hanging fabric silt curtains which allowed water to flow through but prevented heavy debris particles contained in suspension.

## Slide 30
Removal of Marine Growth
Notes: Next phase of works was the removal of oysters and barnacles for the concrete surface.
This was achieved with high pressure water blasting.
A vacuum truck was then used to suck up the debris which was taken to an approved waste facility for disposal

## Slide 31
Rail and Winch Setup
Notes: Rails were then setup in the invert of the culvert to assist with installation of the Channeline profiles.
A winch was setup at the inlet end in preparation to assist with pulling the profile sections into place.

## Slide 32
Installation
Notes: The Channeline profiles were stored off site to reduce site foot print, and were trucked to site each day.
A crane was used to lift and lower the profiles one at a time at the culvert outlet.
The winch line was then used to pull each profile through the culvert to the inlet end.
This process was repeated until all profiles were in place.

## Slide 33
Installation

## Slide 34
End Sealing Prior to Grouting
End seals to host structure
Grout Ports
Notes: Once all profiles were in place the ends were sealed to the host structure and grout ports were installed to enable grouting.

## Slide 35
Grouting
Notes: The annulus was then grouted in 3 in stages or lifts using a flowable cementitious grout, batched of site and delivered in agitators
The grouting was completed in stages to prevent profiles floating or lifting during the grouting process

## Slide 36
Completion
Notes: Finished install

## Slide 37
Project Outcomes
Project completed successfully ​
Cost effective alternative to open trench excavation methods​
Less disruptive to the local community, traffic flows and the environment​
Overall reduced construction duration ​- 12 days from initial mobilisation to site to demob
Notes: Project completed successfully ​
Cost effective alternative to open trench excavation methods​
Less disruptive to the local community, traffic flows and the environment​
Overall reduced construction duration ​- 12 days from initial mobilisation to site to demob

## Slide 38: Questions?